1	gesis® IP+ - Circular connector system IP66/68 - 2-pole - RST20i2	4

1.1	Connector	4

1.1.1	Cable diameter 6-10 mm	4

1.1.1.1	Female with spring clamp connection	4

1.1.1.2	Female with screw connection	10

1.1.1.3	Male with spring clamp connection	15

1.1.1.4	Male with screw connection	19

1.1.2	Cable diameter 10-14 mm	22

1.1.2.1	Female with spring clamp connection	22

1.1.2.2	Female with screw connection	26

1.1.2.3	Male with spring clamp connection	30

1.1.2.4	Male with screw connection	33

1.1.3	For illumination cable 13.3x5.3 - H05RNH2-F2x1.5	36

1.1.3.1	Female with spring clamp connection	36

1.1.3.2	Female with screw connection	38

1.1.3.3	Male with spring clamp connection	40

1.1.3.4	Male with screw connection	42

1.1.4	For AS-i profile cable	44

1.1.4.1	Female with spring clamp connection	44

1.1.4.2	Female with screw connection	46

1.1.4.3	Male with spring clamp connection	48

1.1.4.4	Male with screw connection	50

1.2	Device connector	52

1.2.1	M16	52

1.2.1.1	Female with spring clamp connection	52

1.2.1.2	Female with screw connection	55

1.2.1.3	Male with spring clamp connection	58

1.2.1.4	Male with screw connection	61

1.2.2	M20	64

1.2.2.1	Female with spring clamp connection	64

1.2.2.2	Female with screw connection	67

1.2.2.3	Male with spring clamp connection	70

1.2.2.4	Male with screw connection	73

1.2.3	M25	76

1.2.3.1	Female with spring clamp connection	76

1.2.3.2	Female with screw connection	80

1.2.3.3	Male with spring clamp connection	83

1.2.3.4	Male with screw connection	87

1.3	Distribution block	90

1.4	Accessories	95

1.5	Cable assemblies	98

1.5.1	Cable assemblies, 1.5 mm², containing halogen	98

1.5.2	Cable assemblies, 1.5 mm², insulating rubber compound	101

1.5.3	Cable assemblies, 1.5 mm², AS-i, 24 V auxiliary voltage, LED, 16 A, containing halogen	104

1.5.4	Cable assemblies, 2.5 mm², AS-i, 24 V auxiliary voltage, LED, 20 A, containing halogen	106

2	gesis® IP+ - Circular connector system IP66/68 - 3-pole - RST20i3	108

2.1	Connector	108

2.1.1	Cable diameter 6-10 mm	108

2.1.1.1	Female with spring clamp connection	108

2.1.1.2	Female with screw connection	114

2.1.1.3	Female with crimp connection	119

2.1.1.4	Male with spring clamp connection	121

2.1.1.5	Male with screw connection	126

2.1.1.6	Male with crimp connection,	130

2.1.2	Cable diameter 10-14 mm	132

2.1.2.1	Female with spring clamp connection	132

2.1.2.2	Female with screw connection	138

2.1.2.3	Female with crimp connection	143

2.1.2.4	Male with spring clamp connection	145

2.1.2.5	Male with screw connection	150

2.1.2.6	Male with crimp connection,	154

2.1.3	Cable diameter 13-18 mm	156

2.1.3.1	Female with screw connection	156

2.1.3.2	Female with crimp connection	158

2.1.3.3	Male with screw connection	159

2.1.3.4	Male with crimp connection,	161

2.2	Device connector	162

2.2.1	M16	162

2.2.1.1	Female with spring clamp connection	162

2.2.1.2	Female with screw connection	167

2.2.1.3	Female with crimp connection	171

2.2.1.4	Male with spring clamp connection	173

2.2.1.5	Male with screw connection	178

2.2.1.6	Male with crimp connection,	182

2.2.2	M20	184

2.2.2.1	Female with spring clamp connection	184

2.2.2.2	Female with screw connection	189

2.2.2.3	Female with crimp connection	193

2.2.2.4	Male with spring clamp connection	195

2.2.2.5	Male with screw connection	200

2.2.2.6	Male with crimp connection,	204

2.2.3	M25	206

2.2.3.1	Female with spring clamp connection	206

2.2.3.2	Female with screw connection	211

2.2.3.3	Female with crimp connection	215

2.2.3.4	Male with spring clamp connection	217

2.2.3.5	Male with screw connection	222

2.2.3.6	Male with crimp connection,	226

2.3	Distribution block	228

2.4	Accessories	232

2.5	Cable assemblies	237

2.5.1	Cable assemblies, 1.5 mm², containing halogen	237

2.5.2	Cable assemblies, 1.5 mm², insulating rubber compound	240

2.5.3	Cable assemblies, 2.5 mm², containing halogen	244

2.5.4	Cable assemblies, 2.5 mm², insulating rubber compound	246

3	gesis® IP+ - Circular connector system IP66/68 - 4-pole - RST20i4	248

3.1	Connector	248

3.1.1	Cable diameter 6-10 mm	248

3.1.1.1	Female with screw connection	248

3.1.1.2	Female with crimp connection	252

3.1.1.3	Male with screw connection	254

3.1.1.4	Male with crimp connection,	257

3.1.2	Cable diameter 10-14 mm	259

3.1.2.1	Female with screw connection	259

3.1.2.2	Female with crimp connection	262

3.1.2.3	Male with screw connection	264

3.1.2.4	Male with crimp connection,	266

3.1.3	Cable diameter 13-18 mm	268

3.1.3.1	Female with screw connection	268

3.1.3.2	Female with crimp connection	269

3.1.3.3	Male with screw connection	270

3.1.3.4	Male with crimp connection,	271

3.1.4	1x AS-i profile cable	272

3.1.4.1	Female with screw connection	272

3.1.4.2	Male with screw connection	273

3.1.5	2x AS-i profile cable	274

3.1.5.1	Female with screw connection	274

3.1.5.2	Male with screw connection	275

3.2	Device connector	276

3.2.1	M16	276

3.2.1.1	Female with screw connection	276

3.2.1.2	Female with crimp connection	279

3.2.1.3	Male with screw connection	281

3.2.1.4	Male with crimp connection,	284

3.2.2	M20	286

3.2.2.1	Female with screw connection	286

3.2.2.2	Female with crimp connection	289

3.2.2.3	Male with screw connection	291

3.2.2.4	Male with crimp connection,	294

3.2.3	M25	296

3.2.3.1	Female with screw connection	296

3.2.3.2	Female with crimp connection	299

3.2.3.3	Male with screw connection	301

3.2.3.4	Male with crimp connection,	304

3.3	Distribution block	306

3.4	Accessories	308

3.5	Cable assemblies	313

3.5.1	Cable assemblies, 1.5 mm², containing halogen	313

3.5.2	Cable assemblies, 1.5 mm², insulating rubber compound	315

3.5.3	Cable assemblies, 2.5 mm², containing halogen	316

3.5.4	Cable assemblies, 2.5 mm², insulating rubber compound	317

3.5.5	Cable assemblies, 1.5 mm², mains 4-pole, containing halogen	318

3.5.6	Cable assemblies, 2.5 mm², AS-i 24 V, 20 A, containing halogen	319

4	gesis® IP+ - Circular connector system IP66/68 - 5-pole - RST20i5	320

4.1	Connector	320

4.1.1	Cable diameter 6-10 mm	320

4.1.1.1	Female with screw connection	320

4.1.1.2	Female with crimp connection	326

4.1.1.3	Male with screw connection	330

4.1.1.4	Male with crimp connection,	334

4.1.2	Cable diameter 10-14 mm	338

4.1.2.1	Female with screw connection	338

4.1.2.2	Female with crimp connection	344

4.1.2.3	Male with screw connection	348

4.1.2.4	Male with crimp connection,	352

4.1.3	Cable diameter 13-18 mm	356

4.1.3.1	Female with screw connection	356

4.1.3.2	Female with crimp connection	358

4.1.3.3	Male with screw connection	360

4.1.3.4	Male with crimp connection,	362

4.2	Device connector	364

4.2.1	M16	364

4.2.1.1	Female with screw connection	364

4.2.1.2	Female with crimp connection	368

4.2.1.3	Male with screw connection	372

4.2.1.4	Male with crimp connection,	376

4.2.2	M20	380

4.2.2.1	Female with screw connection	380

4.2.2.2	Female with crimp connection	384

4.2.2.3	Male with screw connection	388

4.2.2.4	Male with crimp connection,	392

4.2.3	M25	396

4.2.3.1	Female with screw connection	396

4.2.3.2	Female with crimp connection	400

4.2.3.3	Male with screw connection	404

4.2.3.4	Male with crimp connection,	408

4.3	Distribution block	412

4.4	Accessories	413

4.5	Cable assemblies	418

4.5.1	Cable assemblies, 1.5 mm², containing halogen	418

4.5.2	Cable assemblies, 1.5 mm², insulating rubber compound	420

4.5.3	Cable assemblies, 2.5 mm², containing halogen	422

4.5.4	Cable assemblies, 2.5 mm², insulating rubber compound	424

4.5.5	Cable assemblies, 4.0 mm², containing halogen	426

4.5.6	Cable assemblies, 4.0 mm², insulating rubber compound	428

4.5.7	Cable assemblies, 2.5 mm², 20 A, mains 5-pole, containing halogen	430

# gesis® IP+ - Circular connector system IP66/68 - 2-pole - RST20i2

## Connector

## Cable diameter 6-10 mm

### Female with spring clamp connection

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1 GL

Part No.: 96.021.0053.0

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1 GL

Part No.: 96.023.0053.0

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRX GL

Part No.: 96.021.0253.0

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1 SW

Part No.: 96.021.0053.1

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1 SW

Part No.: 96.023.0053.1

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRX SW

Part No.: 96.021.0253.1

gesis® circular connector, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1S L BR01

Part No.: 96.021.0051.4

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1 L BR01

Part No.: 96.023.0051.4

gesis® circular connector, IP66/68, splitter connector, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRXS L BR01

Part No.: 96.021.0251.4

gesis® circular connector, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1S L KG06

Part No.: 96.021.0050.8

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1S L KG06

Part No.: 96.023.0050.8

gesis® circular connector, IP66/68, splitter connector, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRXS L KG06

Part No.: 96.021.0250.8

### Female with screw connection

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1 GL

Part No.: 96.021.4053.0

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1 GL

Part No.: 96.023.4053.0

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRX GL

Part No.: 96.021.4253.0

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1 SW

Part No.: 96.021.4053.1

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1 SW

Part No.: 96.023.4053.1

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRX SW

Part No.: 96.021.4253.1

gesis® circular connector, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1S L BR01

Part No.: 96.021.4051.4

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1S L BR01

Part No.: 96.023.4051.4

gesis® circular connector, IP66/68, splitter connector, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRXS L BR01

Part No.: 96.021.4251.4

gesis® circular connector, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1S L KG06

Part No.: 96.021.4050.8

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1S L KG06

Part No.: 96.023.4050.8

gesis® circular connector, IP66/68, splitter connector, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRXS L KG06

Part No.: 96.021.4250.8

### Male with spring clamp connection

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1 GL

Part No.: 96.022.0053.0

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1 GL

Part No.: 96.024.0053.0

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1 SW

Part No.: 96.022.0053.1

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1 SW

Part No.: 96.024.0053.1

gesis® circular connector, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1S L BR01

Part No.: 96.022.0051.4

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1 L BR01

Part No.: 96.024.0051.4

gesis® circular connector, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1S L KG06

Part No.: 96.022.0050.8

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1S L KG06

Part No.: 96.024.0050.8

### Male with screw connection

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1 GL

Part No.: 96.022.4053.0

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1 GL

Part No.: 96.024.4053.0

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1 SW

Part No.: 96.022.4053.1

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1 SW

Part No.: 96.024.4053.1

gesis® circular connector, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1S L BR01

Part No.: 96.022.4051.4

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1S L BR01

Part No.: 96.024.4051.4

gesis® circular connector, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1S L KG06

Part No.: 96.022.4050.8

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1S L KG06

Part No.: 96.024.4050.8

## Cable diameter 10-14 mm

### Female with spring clamp connection

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1 GL

Part No.: 96.021.0153.0

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1 GL

Part No.: 96.023.0153.0

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRX GL

Part No.: 96.021.0353.0

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1 SW

Part No.: 96.021.0153.1

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1 SW

Part No.: 96.023.0153.1

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRX SW

Part No.: 96.021.0353.1

gesis® circular connector, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZR1S L BR01

Part No.: 96.021.0151.4

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YR1 L BR01

Part No.: 96.023.0151.4

gesis® circular connector, IP66/68, splitter connector, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRXS L BR01

Part No.: 96.021.0351.4

### Female with screw connection

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1 GL

Part No.: 96.021.4153.0

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1 GL

Part No.: 96.023.4153.0

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRX GL

Part No.: 96.021.4353.0

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1 SW

Part No.: 96.021.4153.1

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1 SW

Part No.: 96.023.4153.1

gesis® circular connector, IP66/68, splitter connector, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRX SW

Part No.: 96.021.4353.1

gesis® circular connector, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZR1S L BR01

Part No.: 96.021.4151.4

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YR1S L BR01

Part No.: 96.023.4151.4

gesis® circular connector, IP66/68, splitter connector, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRXS L BR01

Part No.: 96.021.4351.4

### Male with spring clamp connection

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1 GL

Part No.: 96.022.0153.0

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1 GL

Part No.: 96.024.0153.0

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1 SW

Part No.: 96.022.0153.1

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1 SW

Part No.: 96.024.0153.1

gesis® circular connector, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZR1S L BR01

Part No.: 96.022.0151.4

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YR1 L BR01

Part No.: 96.024.0151.4

### Male with screw connection

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1 GL

Part No.: 96.022.4153.0

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1 GL

Part No.: 96.024.4153.0

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1 SW

Part No.: 96.022.4153.1

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1 SW

Part No.: 96.024.4153.1

gesis® circular connector, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZR1S L BR01

Part No.: 96.022.4151.4

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YR1S L BR01

Part No.: 96.024.4151.4

## For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

### Female with spring clamp connection

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRW GL

Part No.: 96.021.0453.0

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YRW GL

Part No.: 96.023.0453.0

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRW SW

Part No.: 96.021.0453.1

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YRW SW

Part No.: 96.023.0453.1

### Female with screw connection

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRW GL

Part No.: 96.021.4453.0

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YRW GL

Part No.: 96.023.4453.0

gesis® circular connector, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRW SW

Part No.: 96.021.4453.1

gesis® circular connector, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YRW SW

Part No.: 96.023.4453.1

### Male with spring clamp connection

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZRW GL

Part No.: 96.022.0453.0

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YRW GL

Part No.: 96.024.0453.0

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZRW SW

Part No.: 96.022.0453.1

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YRW SW

Part No.: 96.024.0453.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZRW GL

Part No.: 96.022.4453.0

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YRW GL

Part No.: 96.024.4453.0

gesis® circular connector, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZRW SW

Part No.: 96.022.4453.1

gesis® circular connector, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For illumination cable 13.3x5.3 - H05RNH2-F2x1.5

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YRW SW

Part No.: 96.024.4453.1

## For AS-i profile cable

### Female with spring clamp connection

gesis® circular connector, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRASS L BR01

Part No.: 96.021.0951.4

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YRAS L BR01

Part No.: 96.023.0951.4

gesis® circular connector, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23ZRASS L KG06

Part No.: 96.021.0950.8

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23YRASS L KG06

Part No.: 96.023.0950.8

### Female with screw connection

gesis® circular connector, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRASS L BR01

Part No.: 96.021.4951.4

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YRASS L BR01

Part No.: 96.023.4951.4

gesis® circular connector, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13ZRASS L KG06

Part No.: 96.021.4950.8

gesis® circular connector, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13YRASS L KG06

Part No.: 96.023.4950.8

### Male with spring clamp connection

gesis® circular connector, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZRASS L BR01

Part No.: 96.022.0951.4

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YRAS L BR01

Part No.: 96.024.0951.4

gesis® circular connector, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23ZRASS L KG06

Part No.: 96.022.0950.8

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23YRASS L KG06

Part No.: 96.024.0950.8

### Male with screw connection

gesis® circular connector, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZRASS L BR01

Part No.: 96.022.4951.4

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YRASS L BR01

Part No.: 96.024.4951.4

gesis® circular connector, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13ZRASS L KG06

Part No.: 96.022.4950.8

gesis® circular connector, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 2-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

For AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13YRASS L KG06

Part No.: 96.024.4950.8

## Device connector

### M16

### Female with spring clamp connection

gesis® device connector M16, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M03 GL

Part No.: 96.021.2153.0

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M13 GL

Part No.: 96.025.2153.0

gesis® device connector M16, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M03 SW

Part No.: 96.021.2153.1

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M13 SW

Part No.: 96.025.2153.1

gesis® device connector M16, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M03L BR01

Part No.: 96.021.2151.4

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M13L BR01

Part No.: 96.025.2151.4

gesis® device connector M16, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M03 KG06

Part No.: 96.021.2150.8

### Female with screw connection

gesis® device connector M16, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M03 GL

Part No.: 96.021.6153.0

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M13 GL

Part No.: 96.025.6153.0

gesis® device connector M16, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M03 SW

Part No.: 96.021.6153.1

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M13 SW

Part No.: 96.025.6153.1

gesis® device connector M16, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M03L BR01

Part No.: 96.021.6151.4

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M13L BR01

Part No.: 96.025.6151.4

gesis® device connector M16, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M03 KG06

Part No.: 96.021.6150.8

gesis® device connector M16, IP66/68, female, 7° angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M13L KG06

Part No.: 96.025.6150.8

### Male with spring clamp connection

gesis® device connector M16, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M03 GL

Part No.: 96.022.2153.0

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M13 GL

Part No.: 96.026.2153.0

gesis® device connector M16, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M03 SW

Part No.: 96.022.2153.1

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M13 SW

Part No.: 96.026.2153.1

gesis® device connector M16, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M03L BR01

Part No.: 96.022.2151.4

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M13L BR01

Part No.: 96.026.2151.4

gesis® device connector M16, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M03 KG06

Part No.: 96.022.2150.8

### Male with screw connection

gesis® device connector M16, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M03 GL

Part No.: 96.022.6153.0

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M13 GL

Part No.: 96.026.6153.0

gesis® device connector M16, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M03 SW

Part No.: 96.022.6153.1

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M13 SW

Part No.: 96.026.6153.1

gesis® device connector M16, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M03L BR01

Part No.: 96.022.6151.4

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M13L BR01

Part No.: 96.026.6151.4

gesis® device connector M16, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M03 KG06

Part No.: 96.022.6150.8

gesis® device connector M16, IP66/68, male, 7° angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M13 KG06

Part No.: 96.026.6150.8

### M20

### Female with spring clamp connection

gesis® device connector M20, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M00 GL

Part No.: 96.021.2053.0

gesis® device connector M20, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M10 GL

Part No.: 96.023.2053.0

gesis® device connector M20, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M00 SW

Part No.: 96.021.2053.1

gesis® device connector M20, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M10 SW

Part No.: 96.023.2053.1

gesis® device connector M20, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M00L BR01

Part No.: 96.021.2051.4

gesis® device connector M20, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M10L BR01

Part No.: 96.023.2051.4

gesis® device connector M20, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M10 KG06

Part No.: 96.023.2050.8

### Female with screw connection

gesis® device connector M20, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M00 GL

Part No.: 96.021.6053.0

gesis® device connector M20, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M10 GL

Part No.: 96.023.6053.0

gesis® device connector M20, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M00 SW

Part No.: 96.021.6053.1

gesis® device connector M20, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M10 SW

Part No.: 96.023.6053.1

gesis® device connector M20, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M00L BR01

Part No.: 96.021.6051.4

gesis® device connector M20, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M10L BR01

Part No.: 96.023.6051.4

gesis® device connector M20, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M00 KG06

Part No.: 96.021.6050.8

gesis® device connector M20, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M10 KG06

Part No.: 96.023.6050.8

### Male with spring clamp connection

gesis® device connector M20, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M00 GL

Part No.: 96.022.2053.0

gesis® device connector M20, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M10 GL

Part No.: 96.024.2053.0

gesis® device connector M20, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M00 SW

Part No.: 96.022.2053.1

gesis® device connector M20, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M10 SW

Part No.: 96.024.2053.1

gesis® device connector M20, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M00L BR01

Part No.: 96.022.2051.4

gesis® device connector M20, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M10L BR01

Part No.: 96.024.2051.4

gesis® device connector M20, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M10 KG06

Part No.: 96.024.2050.8

### Male with screw connection

gesis® device connector M20, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M00 GL

Part No.: 96.022.6053.0

gesis® device connector M20, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M10 GL

Part No.: 96.024.6053.0

gesis® device connector M20, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M00 SW

Part No.: 96.022.6053.1

gesis® device connector M20, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M10 SW

Part No.: 96.024.6053.1

gesis® device connector M20, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M00L BR01

Part No.: 96.022.6051.4

gesis® device connector M20, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M10L BR01

Part No.: 96.024.6051.4

gesis® device connector M20, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M00 KG06

Part No.: 96.022.6050.8

gesis® device connector M20, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M10 KG06

Part No.: 96.024.6050.8

### M25

### Female with spring clamp connection

gesis® device connector M25, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M01 GL

Part No.: 96.021.1053.0

gesis® device connector M25, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M11 GL

Part No.: 96.023.1053.0

gesis® device connector M25, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M01 SW

Part No.: 96.021.1053.1

gesis® device connector M25, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M11 SW

Part No.: 96.023.1053.1

gesis® device connector M25, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M01L BR01

Part No.: 96.021.1051.4

gesis® device connector M25, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M11L BR01

Part No.: 96.023.1051.4

gesis® device connector M25, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M01 KG06

Part No.: 96.021.1050.8

gesis® device connector M25, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F B23M11 KG06

Part No.: 96.023.1050.8

### Female with screw connection

gesis® device connector M25, IP66/68, female, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M01 GL

Part No.: 96.021.5053.0

gesis® device connector M25, IP66/68, female, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M11 GL

Part No.: 96.023.5053.0

gesis® device connector M25, IP66/68, female, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M01 SW

Part No.: 96.021.5053.1

gesis® device connector M25, IP66/68, female, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M11 SW

Part No.: 96.023.5053.1

gesis® device connector M25, IP66/68, female, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M01L BR01

Part No.: 96.021.5051.4

gesis® device connector M25, IP66/68, female, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M11L BR01

Part No.: 96.023.5051.4

gesis® device connector M25, IP66/68, female, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M01 KG06

Part No.: 96.021.5050.8

gesis® device connector M25, IP66/68, female, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: +, -

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S B13M11 KG06

Part No.: 96.023.5050.8

### Male with spring clamp connection

gesis® device connector M25, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M01 GL

Part No.: 96.022.1053.0

gesis® device connector M25, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M11 GL

Part No.: 96.024.1053.0

gesis® device connector M25, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M01 SW

Part No.: 96.022.1053.1

gesis® device connector M25, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M11 SW

Part No.: 96.024.1053.1

gesis® device connector M25, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M01L BR01

Part No.: 96.022.1051.4

gesis® device connector M25, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M11L BR01

Part No.: 96.024.1051.4

gesis® device connector M25, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M01 KG06

Part No.: 96.022.1050.8

gesis® device connector M25, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2F S23M11 KG06

Part No.: 96.024.1050.8

### Male with screw connection

gesis® device connector M25, IP66/68, male, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M01 GL

Part No.: 96.022.5053.0

gesis® device connector M25, IP66/68, male, angled, 2-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M11 GL

Part No.: 96.024.5053.0

gesis® device connector M25, IP66/68, male, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M01 SW

Part No.: 96.022.5053.1

gesis® device connector M25, IP66/68, male, angled, 2-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M11 SW

Part No.: 96.024.5053.1

gesis® device connector M25, IP66/68, male, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M01L BR01

Part No.: 96.022.5051.4

gesis® device connector M25, IP66/68, male, angled, 2-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M11L BR01

Part No.: 96.024.5051.4

gesis® device connector M25, IP66/68, male, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M01 KG06

Part No.: 96.022.5050.8

gesis® device connector M25, IP66/68, male, angled, 2-pole, low voltage, pebble gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 2-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: -, +

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2S S13M11 KG06

Part No.: 96.024.5050.8

## Distribution block

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, with mounting option, 250 V, 20 A, gray

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (parallel connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 F V GL

Part No.: 96.020.0153.0

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, 250 V, 20 A, gray

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (parallel connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 V GL

Part No.: 96.020.0253.0

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, with mounting option, 250 V, 20 A, black

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (parallel connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 F V SW

Part No.: 96.020.0153.1

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, 250 V, 20 A, black

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (parallel connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 V SW

Part No.: 96.020.0253.1

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, with mounting option, low voltage, brown

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (parallel connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 F V L BR01

Part No.: 96.020.0151.4

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, low voltage, brown

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 V L BR01

Part No.: 96.020.0251.4

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, serial connection, with mounting option, low voltage, brown

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (serial connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2B 3R1 V L BR01

Part No.: 99.910.0000.7

gesis® Jumper plug, IP66/68, 2-pole, low voltage, brown

System gesis® IP+ - Jumper plug for unused slots on the serial distribution block according to IEC 61535, 2-pole, turned contacts, with integrated locking, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2B L BR01

Part No.: 99.537.0000.7

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, with mounting option, low voltage, pebble gray

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block (parallel connection), H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 F V L KG06

Part No.: 96.020.0150.8

gesis® Distribution block, IP66/68, 2-pole, 1 input, 3 outputs, parallel connection, low voltage, pebble gray

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 2-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical/color coding pebble gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2V 3P1 V L KG06

Part No.: 96.020.0250.8

gesis® compact distribution unit, IP66/68, 2-pole, 1 input, 3 outputs, 250 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to four M25 device connectors IP66/68, 2-pole, 1 input, 3 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Dimension: 104x162x57.2 mm

Brand: Wieland Electric GmbH

Type: RST20I2B 3P1 F VG SW

gesis® multi distribution unit, IP66/68, 2-pole, 1 input, 7 outputs, 250 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to eight M25 device connectors IP66/68, 2-pole, 1 input, 7 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 7

Halogen-free: yes

Dimension: 104x162x96 mm

Brand: Wieland Electric GmbH

Type: RST20I2B 7P1 F VG SW

Part No.: 99.946.0000.7

## Accessories

gesis® Cover piece IP66/68 for male, 2-3-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS GL

Part No.: 99.415.6205.2

gesis® Cover piece IP66/68 for male, 2-3-pole, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS GL

Part No.: 05.564.4453.0

gesis® Cover piece IP66/68 for male, 2-3-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: 99.416.6205.2

gesis® Cover piece IP66/68 for male, 2-3-pole, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: 05.564.4453.1

gesis® Cover piece IP66/68 for female, 2-3-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i2, with locking, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS GL

Part No.: 99.413.6205.2

gesis® Cover piece IP66/68 for female, 2-3-pole, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS GL

Part No.: Z5.564.4553.0

gesis® Cover piece IP66/68 for female, 2-3-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: 99.414.6205.2

gesis® Cover piece IP66/68 for female, 2-3-pole, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I2 VS SW

Part No.: Z5.564.4553.1

gesis® Mounting plate for splitter connector, gray

System gesis® IP+ - Mounting plate for splitter connector RST20i2, gray.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG GR

Part No.: 01.006.1553.0

gesis® Mounting plate for splitter connector, black

System gesis® IP+ - Mounting plate for splitter connector RST20i2, black.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG SW

Part No.: 01.006.1553.1

## Cable assemblies

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 15P x0SW

Part No.: 96.222.x000.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled H05VV-F extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 15PL x0BR01

Part No.: 96.222.x002.4 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 15P x0SW

Part No.: 96.222.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled H05VV-F connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 15PL x0BR01

Part No.: 96.222.x007.4 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 15P x0SW

Part No.: 96.222.x004.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled H05VV-F connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 15PL x0BR01

Part No.: 96.222.x008.4 (x corresponds to length in m)

gesis® cable, female, European male connector SKII, 2x 1.5 mm², 250 V, 16 A, length: 1.5 m, gray

System gesis® IP+ - assembled H05VV-F cable, 2-pole, 1.5 mm², female RST20i2 with European male connector SKII, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H05VV-F

Cable color: gray

Halogen-free: no

Length: 1.5 m

Brand: Wieland Electric GmbH

Type: RST20I2K1BI 15P 15GL

Part No.: 99.710.0000.7

gesis® cable, female, European male connector SKII, 2x 1.5 mm², 250 V, 16 A, length: 2.5 m, gray

System gesis® IP+ - assembled H05VV-F cable, 2-pole, 1.5 mm², female RST20i2 with European male connector SKII, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H05VV-F

Cable color: gray

Halogen-free: no

Length: 2.5 m

Brand: Wieland Electric GmbH

Type: RST20I2K1BI 15P 25GL

Part No.: 99.711.0000.7

### Cable assemblies, 1.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 15 x0SW

Part No.: 96.222.x030.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled H07RN-F extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 15L x0BR01

Part No.: 96.222.x032.4 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 15 x0SW

Part No.: 96.222.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled H07RN-F connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 15L x0BR01

Part No.: 96.222.x037.4 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 15 x0SW

Part No.: 96.222.x034.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled H07RN-F connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 15L x0BR01

Part No.: 96.222.x038.4 (x corresponds to length in m)

gesis® cable, female, European male connector SKII, 2x 1.5 mm², 250 V, 16 A, length: 1.5 m, black

System gesis® IP+ - assembled H07RN-F cable, 2-pole, 1.5 mm², female RST20i2 with European male connector SKII, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 1.5 m

Brand: Wieland Electric GmbH

Type: RST20I2K1BI 15 15SW

Part No.: 99.708.0000.7

gesis® cable, female, European male connector SKII, 2x 1.5 mm², 250 V, 16 A, length: 2.5 m, black

System gesis® IP+ - assembled H07RN-F cable, 2-pole, 1.5 mm², female RST20i2 with European male connector SKII, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 2.5 m

Brand: Wieland Electric GmbH

Type: RST20I2K1BI 15 25SW

Part No.: 99.709.0000.7

### Cable assemblies, 1.5 mm², AS-i, 24 V auxiliary voltage, LED, 16 A, containing halogen

gesis® extension cable IP66/68, female, male, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled Ölflex Classic 100 extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 15PL x0BR01

Part No.: 96.222.x092.4 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 2x 1.5 mm², 24 V, 16 A, length: x m, pebble gray

System gesis® IP+ - assembled Ölflex Classic 100 extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical/color coding pebble gray.

Rated voltage: 24 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 15P x0KG06

Part No.: 96.222.x092.8 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 15PL x0BR01

Part No.: 96.222.x097.4 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 1.5 mm², 24 V, 16 A, length: x m, pebble gray

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding pebble gray.

Rated voltage: 24 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 15P x0KG06

Part No.: 96.222.x097.8 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 1.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: pebble gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 15PL x0BR01

Part No.: 96.222.x098.4 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 1.5 mm², 24 V, 16 A, length: x m, pebble gray

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding pebble gray.

Rated voltage: 4 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 15P x0KG06

Part No.: 96.222.x098.8 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², AS-i, 24 V auxiliary voltage, LED, 20 A, containing halogen

gesis® extension cable IP66/68, female, male, 2x 2.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled Ölflex Classic 100 extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 25PL x0BR01

Part No.: 96.223.x092.4 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 2x 2.5 mm², 24 V, 20 A, length: x m, pebble gray

System gesis® IP+ - assembled Ölflex Classic 100 extension cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, female RST20i2, according to IEC 61535, mechanical/color coding pebble gray.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1BS 25P x0KG06

Part No.: 96.223.x092.8 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 2.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 25PL x0BR01

Part No.: 96.223.x097.4 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 2x 2.5 mm², 24 V, 20 A, length: x m, pebble gray

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², female RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding pebble gray.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1B 25P x0KG06

Part No.: 96.223.x097.8 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 2.5 mm², low voltage, length: x m, brown

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: pebble gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 25PL x0BR01

Part No.: 96.223.x098.4 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 2x 2.5 mm², 24 V, 20 A, length: x m, pebble gray

System gesis® IP+ - assembled Ölflex Classic 100 connection cable IP66/68, 2-pole, 1.5 mm², with locking, male RST20i2, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding pebble gray.

Rated voltage: 4 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 100

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I2K1S 25P x0KG06

Part No.: 96.223.x098.8 (x corresponds to length in m)

# gesis® IP+ - Circular connector system IP66/68 - 3-pole - RST20i3

## Connector

## Cable diameter 6-10 mm

### Female with spring clamp connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR1 GL

Part No.: 96.031.0053.0

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR1 GL

Part No.: 96.033.0053.0

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZRX GL

Part No.: 96.031.0253.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR1 SW

Part No.: 96.031.0053.1

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR1 SW

Part No.: 96.033.0053.1

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZRX SW

Part No.: 96.031.0253.1

gesis® circular connector, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR1SH GN02

Part No.: 96.031.0055.7

gesis® circular connector, IP66/68, female, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR1SH GN02

Part No.: 96.033.0055.7

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZRXSH GN02

Part No.: 96.031.0255.7

gesis® circular connector, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR1S L BR01

Part No.: 96.031.0051.4

gesis® circular connector, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR1S L BR01

Part No.: 96.033.0051.4

gesis® circular connector, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR1S BL07

Part No.: 96.031.0053.9

gesis® circular connector, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR1S BL07

Part No.: 96.033.0053.9

### Female with screw connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR1 GL

Part No.: 96.031.4053.0

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR1 GL

Part No.: 96.033.4053.0

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZRX GL

Part No.: 96.031.4253.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR1 SW

Part No.: 96.031.4053.1

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR1 SW

Part No.: 96.033.4053.1

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZRX SW

Part No.: 96.031.4253.1

gesis® circular connector, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR1SH GN02

Part No.: 96.031.4055.7

gesis® circular connector, IP66/68, female, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR1SH GN02

Part No.: 96.033.4055.7

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZRXSH GN02

Part No.: 96.031.4255.7

gesis® circular connector, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR1S L BR01

Part No.: 96.031.4051.4

gesis® circular connector, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR1S L BR01

Part No.: 96.033.4051.4

gesis® circular connector, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR1S BL07

Part No.: 96.031.4053.9

gesis® circular connector, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR1S BL07

Part No.: 96.033.4053.9

### Female with crimp connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 ZR1 V GL

Part No.: 96.131.0053.0

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 YR1 V GL

Part No.: 96.133.0053.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 ZR1 V SW

Part No.: 96.131.0053.1

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 YR1 V SW

Part No.: 96.133.0053.1

### Male with spring clamp connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR1 GL

Part No.: 96.032.0053.0

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR1 GL

Part No.: 96.034.0053.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR1 SW

Part No.: 96.032.0053.1

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR1 SW

Part No.: 96.034.0053.1

gesis® circular connector, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR1SH GN02

Part No.: 96.032.0055.7

gesis® circular connector, IP66/68, male, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR1SH GN02

Part No.: 96.034.0055.7

gesis® circular connector, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR1S L BR01

Part No.: 96.032.0051.4

gesis® circular connector, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR1S L BR01

Part No.: 96.034.0051.4

gesis® circular connector, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR1S BL07

Part No.: 96.032.0053.9

gesis® circular connector, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR1S BL07

Part No.: 96.034.0053.9

### Male with screw connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR1 GL

Part No.: 96.032.4053.0

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR1 GL

Part No.: 96.034.4053.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR1 SW

Part No.: 96.032.4053.1

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR1 SW

Part No.: 96.034.4053.1

gesis® circular connector, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR1SH GN02

Part No.: 96.032.4055.7

gesis® circular connector, IP66/68, male, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR1SH GN02

Part No.: 96.034.4055.7

gesis® circular connector, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR1S L BR01

Part No.: 96.032.4051.4

gesis® circular connector, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR1S L BR01

Part No.: 96.034.4051.4

gesis® circular connector, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR1S BL07

Part No.: 96.032.4053.9

gesis® circular connector, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR1S BL07

Part No.: 96.034.4053.9

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 ZR1 V GL

Part No.: 96.132.0053.0

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 YR1 V GL

Part No.: 96.134.0053.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 ZR1 V SW

Part No.: 96.132.0053.1

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 YR1 V SW

Part No.: 96.134.0053.1

## Cable diameter 10-14 mm

### Female with spring clamp connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR2 GL

Part No.: 96.031.0153.0

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR2 GL

Part No.: 96.033.0153.0

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZRY GL

Part No.: 96.031.0353.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR2 SW

Part No.: 96.031.0153.1

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR2 SW

Part No.: 96.033.0153.1

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZRY SW

Part No.: 96.031.0353.1

gesis® circular connector, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR2SH GN02

Part No.: 96.031.0155.7

gesis® circular connector, IP66/68, female, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR2SH GN02

Part No.: 96.033.0155.7

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZRYSH GN02

Part No.: 96.031.0355.7

gesis® circular connector, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR2S L BR01

Part No.: 96.031.0151.4

gesis® circular connector, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR2S L BR01

Part No.: 96.033.0151.4

gesis® circular connector, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 ZR2S BL07

Part No.: 96.031.0153.9

gesis® circular connector, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 YR2S BL07

Part No.: 96.033.0153.9

### Female with screw connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR2 GL

Part No.: 96.031.4153.0

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR2 GL

Part No.: 96.033.4153.0

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZRY GL

Part No.: 96.031.4353.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR2 SW

Part No.: 96.031.4153.1

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR2 SW

Part No.: 96.033.4153.1

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZRY SW

Part No.: 96.031.4353.1

gesis® circular connector, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR2SH GN02

Part No.: 96.031.4155.7

gesis® circular connector, IP66/68, female, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR2SH GN02

Part No.: 96.033.4155.7

gesis® circular connector, IP66/68, splitter connector, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 2.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZRYSH GN02

Part No.: 96.031.4355.7

gesis® circular connector, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR2S L BR01

Part No.: 96.031.4151.4

gesis® circular connector, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR2S L BR01

Part No.: 96.033.4151.4

gesis® circular connector, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR2S BL07

Part No.: 96.031.4153.9

gesis® circular connector, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 YR2S BL07

Part No.: 96.033.4153.9

### Female with crimp connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 ZR2 V GL

Part No.: 96.131.0153.0

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 YR2 V GL

Part No.: 96.133.0153.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 ZR2 V SW

Part No.: 96.131.0153.1

gesis® circular connector, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 YR2 V SW

Part No.: 96.133.0153.1

### Male with spring clamp connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR2 GL

Part No.: 96.032.0153.0

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR2 GL

Part No.: 96.034.0153.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR2 SW

Part No.: 96.032.0153.1

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR2 SW

Part No.: 96.034.0153.1

gesis® circular connector, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR2SH GN02

Part No.: 96.032.0155.7

gesis® circular connector, IP66/68, male, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR2SH GN02

Part No.: 96.034.0155.7

gesis® circular connector, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR2S L BR01

Part No.: 96.032.0151.4

gesis® circular connector, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR2S L BR01

Part No.: 96.034.0151.4

gesis® circular connector, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 ZR2S BL07

Part No.: 96.032.0153.9

gesis® circular connector, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with spring clamp connection, compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 YR2S BL07

Part No.: 96.034.0153.9

### Male with screw connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR2 GL

Part No.: 96.032.4153.0

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR2 GL

Part No.: 96.034.4153.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR2 SW

Part No.: 96.032.4153.1

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR2 SW

Part No.: 96.034.4153.1

gesis® circular connector, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR2SH GN02

Part No.: 96.032.4155.7

gesis® circular connector, IP66/68, male, angled, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR2SH GN02

Part No.: 96.034.4155.7

gesis® circular connector, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR2S L BR01

Part No.: 96.032.4151.4

gesis® circular connector, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR2S L BR01

Part No.: 96.034.4151.4

gesis® circular connector, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR2S BL07

Part No.: 96.032.4153.9

gesis® circular connector, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 YR2S BL07

Part No.: 96.034.4153.9

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 ZR2 V GL

Part No.: 96.132.0153.0

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 YR2 V GL

Part No.: 96.134.0153.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 ZR2 V SW

Part No.: 96.132.0153.1

gesis® circular connector, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 YR2 V SW

Part No.: 96.134.0153.1

## Cable diameter 13-18 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR3 GL

Part No.: 96.031.4553.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR3 SW

Part No.: 96.031.4553.1

gesis® circular connector, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 ZR3SH GN02

Part No.: 96.031.4555.7

### Female with crimp connection

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 ZR3 V GL

Part No.: 96.131.4553.0

gesis® circular connector, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 ZR3 V SW

Part No.: 96.131.4553.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR3 GL

Part No.: 96.032.4553.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR3 SW

Part No.: 96.032.4553.1

gesis® circular connector, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding green.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 6.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 ZR3SH GN02

Part No.: 96.032.4555.7

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 ZR3 V GL

Part No.: 96.132.4553.0

gesis® circular connector, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 3-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 ZR3 V SW

Part No.: 96.132.4553.1

## Device connector

### M16

### Female with spring clamp connection

gesis® device connector M16, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M03 GL

Part No.: 96.031.2153.0

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M13 GL

Part No.: 96.035.2153.0

gesis® device connector M16, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M03 SW

Part No.: 96.031.2153.1

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M13 SW

Part No.: 96.035.2153.1

gesis® device connector M16, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M03H GN02

Part No.: 96.031.2155.7

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M13H GN02

Part No.: 96.035.2155.7

gesis® device connector M16, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M03L BR01

Part No.: 96.031.2151.4

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M13L BR01

Part No.: 96.035.2151.4

gesis® device connector M16, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M03 BL07

Part No.: 96.031.2153.9

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M13 BL07

Part No.: 96.035.2153.9

### Female with screw connection

gesis® device connector M16, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M03 GL

Part No.: 96.031.6153.0

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M13 GL

Part No.: 96.035.6153.0

gesis® device connector M16, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M03 SW

Part No.: 96.031.6153.1

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M13 SW

Part No.: 96.035.6153.1

gesis® device connector M16, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M03H GN02

Part No.: 96.031.6155.7

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M13H GN02

Part No.: 96.035.6155.7

gesis® device connector M16, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M03L BR01

Part No.: 96.031.6151.4

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M13L BR01

Part No.: 96.035.6151.4

gesis® device connector M16, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M03 BL07

Part No.: 96.031.6153.9

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M13 BL07

Part No.: 96.035.6153.9

### Female with crimp connection

gesis® device connector M16, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M03 GL

Part No.: 96.131.2153.0

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M13 GL

Part No.: 96.135.2153.0

gesis® device connector M16, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M03 SW

Part No.: 96.131.2153.1

gesis® device connector M16, IP66/68, female, 7° angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M13 SW

Part No.: 96.135.2153.1

### Male with spring clamp connection

gesis® device connector M16, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M03 GL

Part No.: 96.032.2153.0

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M13 GL

Part No.: 96.036.2153.0

gesis® device connector M16, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M03 SW

Part No.: 96.032.2153.1

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M13 SW

Part No.: 96.036.2153.1

gesis® device connector M16, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M03H GN02

Part No.: 96.032.2155.7

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M13H GN02

Part No.: 96.036.2155.7

gesis® device connector M16, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M03L BR01

Part No.: 96.032.2151.4

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M13L BR01

Part No.: 96.036.2151.4

gesis® device connector M16, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M03 BL07

Part No.: 96.032.2153.9

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M13 BL07

Part No.: 96.036.2153.9

### Male with screw connection

gesis® device connector M16, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M03 GL

Part No.: 96.032.6153.0

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M13 GL

Part No.: 96.036.6153.0

gesis® device connector M16, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M03 SW

Part No.: 96.032.6153.1

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M13 SW

Part No.: 96.036.6153.1

gesis® device connector M16, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M03H GN02

Part No.: 96.032.6155.7

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M13H GN02

Part No.: 96.036.6155.7

gesis® device connector M16, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M03L BR01

Part No.: 96.032.6151.4

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M13L BR01

Part No.: 96.036.6151.4

gesis® device connector M16, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M03 BL07

Part No.: 96.032.6153.9

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M13 BL07

Part No.: 96.036.6153.9

### Male with crimp connection,

gesis® device connector M16, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M03 GL

Part No.: 96.132.2153.0

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M13 GL

Part No.: 96.136.2153.0

gesis® device connector M16, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M03 SW

Part No.: 96.132.2153.1

gesis® device connector M16, IP66/68, male, 7° angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M13 SW

Part No.: 96.136.2153.1

### M20

### Female with spring clamp connection

gesis® device connector M20, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M00 GL

Part No.: 96.031.2053.0

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M10 GL

Part No.: 96.033.2053.0

gesis® device connector M20, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M00 SW

Part No.: 96.031.2053.1

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M10 SW

Part No.: 96.033.2053.1

gesis® device connector M20, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M00H GN02

Part No.: 96.031.2055.7

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M10H GN02

Part No.: 96.033.2055.7

gesis® device connector M20, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M00L BR01

Part No.: 96.031.2051.4

gesis® device connector M20, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M10L BR01

Part No.: 96.033.2051.4

gesis® device connector M20, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M00 BL07

Part No.: 96.031.2053.9

gesis® device connector M20, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M10 BL07

Part No.: 96.033.2053.9

### Female with screw connection

gesis® device connector M20, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M00 GL

Part No.: 96.031.6053.0

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M10 GL

Part No.: 96.033.6053.0

gesis® device connector M20, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M00 SW

Part No.: 96.031.6053.1

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M10 SW

Part No.: 96.033.6053.1

gesis® device connector M20, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M00H GN02

Part No.: 96.031.6055.7

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M10H GN02

Part No.: 96.033.6055.7

gesis® device connector M20, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M00L BR01

Part No.: 96.031.6051.4

gesis® device connector M20, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M10L BR01

Part No.: 96.033.6051.4

gesis® device connector M20, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M00 BL07

Part No.: 96.031.6053.9

gesis® device connector M20, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M10 BL07

Part No.: 96.033.6053.9

### Female with crimp connection

gesis® device connector M20, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M00 GL

Part No.: 96.131.2053.0

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M10 GL

Part No.: 96.133.2053.0

gesis® device connector M20, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M00 SW

Part No.: 96.131.2053.1

gesis® device connector M20, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M10 SW

Part No.: 96.133.2053.1

### Male with spring clamp connection

gesis® device connector M20, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M00 GL

Part No.: 96.032.2053.0

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M10 GL

Part No.: 96.034.2053.0

gesis® device connector M20, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M00 SW

Part No.: 96.032.2053.1

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M10 SW

Part No.: 96.034.2053.1

gesis® device connector M20, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M00H GN02

Part No.: 96.032.2055.7

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M10H GN02

Part No.: 96.034.2055.7

gesis® device connector M20, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M00L BR01

Part No.: 96.032.2051.4

gesis® device connector M20, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M10L BR01

Part No.: 96.034.2051.4

gesis® device connector M20, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M00 BL07

Part No.: 96.032.2053.9

gesis® device connector M20, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M10 BL07

Part No.: 96.034.2053.9

### Male with screw connection

gesis® device connector M20, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M00 GL

Part No.: 96.032.6053.0

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M10 GL

Part No.: 96.034.6053.0

gesis® device connector M20, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M00 SW

Part No.: 96.032.6053.1

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M10 SW

Part No.: 96.034.6053.1

gesis® device connector M20, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M00H GN02

Part No.: 96.032.6055.7

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M10H GN02

Part No.: 96.034.6055.7

gesis® device connector M20, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M00L BR01

Part No.: 96.032.6051.4

gesis® device connector M20, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M10L BR01

Part No.: 96.034.6051.4

gesis® device connector M20, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M00 BL07

Part No.: 96.032.6053.9

gesis® device connector M20, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M10 BL07

Part No.: 96.034.6053.9

### Male with crimp connection,

gesis® device connector M20, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M00 GL

Part No.: 96.132.2053.0

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M10 GL

Part No.: 96.134.2053.0

gesis® device connector M20, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M00 SW

Part No.: 96.132.2053.1

gesis® device connector M20, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M10 SW

Part No.: 96.134.2053.1

### M25

### Female with spring clamp connection

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M01 GL

Part No.: 96.031.1053.0

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M11 GL

Part No.: 96.033.1053.0

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M01 SW

Part No.: 96.031.1053.1

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M11 SW

Part No.: 96.033.1053.1

gesis® device connector M25, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M01H GN02

Part No.: 96.031.1055.7

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M11H GN02

Part No.: 96.033.1055.7

gesis® device connector M25, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M01L BR01

Part No.: 96.031.1051.4

gesis® device connector M25, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M11L BR01

Part No.: 96.033.1051.4

gesis® device connector M25, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M01 BL07

Part No.: 96.031.1053.9

gesis® device connector M25, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F B2 M11 BL07

Part No.: 96.033.1053.9

### Female with screw connection

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M01 GL

Part No.: 96.031.5053.0

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M11 GL

Part No.: 96.033.5053.0

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M01 SW

Part No.: 96.031.5053.1

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M11 SW

Part No.: 96.033.5053.1

gesis® device connector M25, IP66/68, female, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M01H GN02

Part No.: 96.031.5055.7

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M11H GN02

Part No.: 96.033.5055.7

gesis® device connector M25, IP66/68, female, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M01L BR01

Part No.: 96.031.5051.4

gesis® device connector M25, IP66/68, female, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M11L BR01

Part No.: 96.033.5051.4

gesis® device connector M25, IP66/68, female, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M01 BL07

Part No.: 96.031.5053.9

gesis® device connector M25, IP66/68, female, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S B1 M11 BL07

Part No.: 96.033.5053.9

### Female with crimp connection

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M01 GL

Part No.: 96.131.1053.0

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M11 GL

Part No.: 96.133.1053.0

gesis® device connector M25, IP66/68, female, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M01 SW

Part No.: 96.131.1053.1

gesis® device connector M25, IP66/68, female, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C B1 M11 SW

Part No.: 96.133.1053.1

### Male with spring clamp connection

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M01 GL

Part No.: 96.032.1053.0

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M11 GL

Part No.: 96.034.1053.0

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M01 SW

Part No.: 96.032.1053.1

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M11 SW

Part No.: 96.034.1053.1

gesis® device connector M25, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M01H GN02

Part No.: 96.032.1055.7

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M11H GN02

Part No.: 96.034.1055.7

gesis® device connector M25, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M01L BR01

Part No.: 96.032.1051.4

gesis® device connector M25, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M11L BR01

Part No.: 96.034.1051.4

gesis® device connector M25, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M01 BL07

Part No.: 96.032.1053.9

gesis® device connector M25, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with spring clamp connection, fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, solid: 0.5 - 2.5 mm²

Terminal cross-section, fine-stranded: 0.5 - 1.5 mm²

Terminal cross-section, fine-stranded: 0.75 - 1.5 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3F S2 M11 BL07

Part No.: 96.034.1053.9

### Male with screw connection

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M01 GL

Part No.: 96.032.5053.0

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M11 GL

Part No.: 96.034.5053.0

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M01 SW

Part No.: 96.032.5053.1

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M11 SW

Part No.: 96.034.5053.1

gesis® device connector M25, IP66/68, male, 3-pole, 250/400 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M01H GN02

Part No.: 96.032.5055.7

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, green

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M11H GN02

Part No.: 96.034.5055.7

gesis® device connector M25, IP66/68, male, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M01L BR01

Part No.: 96.032.5051.4

gesis® device connector M25, IP66/68, male, angled, 3-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M11L BR01

Part No.: 96.034.5051.4

gesis® device connector M25, IP66/68, male, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M01 BL07

Part No.: 96.032.5053.9

gesis® device connector M25, IP66/68, male, angled, 3-pole, switching functionality, 250 V, light blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding light blue.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 6.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 2, 1, 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3S S1 M11 BL07

Part No.: 96.034.5053.9

### Male with crimp connection,

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M01 GL

Part No.: 96.132.1053.0

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M11 GL

Part No.: 96.134.1053.0

gesis® device connector M25, IP66/68, male, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M01 SW

Part No.: 96.132.1053.1

gesis® device connector M25, IP66/68, male, angled, 3-pole, 250 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 3-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  N, L, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3C S1 M11 SW

Part No.: 96.134.1053.1

## Distribution block

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, with mounting option, 250 V, 20 A, gray

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 F V GL

Part No.: 96.030.0153.0

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, 250 V, 20 A, gray

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 V GL

Part No.: 96.030.0253.0

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, with mounting option, 250 V, 20 A, black

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 F V SW

Part No.: 96.030.0153.1

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, 250 V, 20 A, black

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 V SW

Part No.: 96.030.0253.1

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, with mounting option, 250 V, 20 A, green

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 F V H GN02

Part No.: 96.030.0155.7

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, 250 V, 20 A, green

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 V H GN02

Part No.: 96.030.0255.7

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, with mounting option, low voltage, brown

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, with mounting option, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 F V L BR01

Part No.: 96.030.0151.4

gesis® Distribution block, IP66/68, 3-pole, 1 input, 3 outputs, low voltage, brown

System gesis® IP+ - Distribution block for circular connector IP66/68 according to IEC 61535, combined distribution block, H shaped, 3-pole, turned contacts, 1 input, 3 outputs, with integrated locking, mechanical/color coding brown.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3V 3P1 V L BR01

Part No.: 96.030.0251.4

gesis® compact distribution unit, IP66/68, 3-pole, 1 input, 3 outputs, 250 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to four M25 device connectors IP66/68, 3-pole, 1 input, 3 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Dimension: 104x162x57.2 mm

Brand: Wieland Electric GmbH

Type: RST20I3B 3P1 F VG SW

Part No.: 99.906.0000.7

gesis® multi distribution unit, IP66/68, 3-pole, 1 input, 7 outputs, 250 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to eight M25 device connectors IP66/68, 3-pole, 1 input, 7 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 7

Halogen-free: yes

Dimension: 104x162x96 mm

Brand: Wieland Electric GmbH

Type: RST20I3B 7P1 F VG SW

Part No.: 99.929.0000.7

## Accessories

gesis® Cover piece IP66/68 for male, 2-3-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS GL

Part No.: 99.415.6205.2

gesis® Cover piece IP66/68 for male, 2-3-pole, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS GL

Part No.: 05.564.4453.0

gesis® Cover piece IP66/68 for male, 2-3-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS SW

Part No.: 99.416.6205.2

gesis® Cover piece IP66/68 for male, 2-3-pole, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i2 and RST20i3, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS SW

Part No.: 05.564.4453.1

gesis® Cover piece IP66/68 for female, 2-3-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS GL

Part No.: 99.413.6205.2

gesis® Cover piece IP66/68 for female, 2-3-pole, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS GL

Part No.: Z5.564.4553.0

gesis® Cover piece IP66/68 for female, 2-3-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS SW

Part No.: 99.414.6205.2

gesis® Cover piece IP66/68 for female, 2-3-pole, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i2 and RST20i3, with locking, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I3 VS SW

Part No.: Z5.564.4553.1

gesis® Mounting plate for splitter connector, gray

System gesis® IP+ - Mounting plate for splitter connector RST20i3, gray.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG GR

Part No.: 01.006.1553.0

gesis® Mounting plate for splitter connector, black

System gesis® IP+ - Mounting plate for splitter connector RST20i3, black.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG SW

Part No.: 01.006.1553.1

gesis® crimp contact, female, 0.75 - 1.0 mm², with marking 1

System gesis® IP+ - Crimp contact, female, for circular connector RST20i3, with marking (groove).

Terminal cross-section, fine-stranded: 0.75 - 1.0 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I3C B 75 10

Part No.: 02.122.9000.0

gesis® crimp contact, female, 1.5 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST20i3, without marking (groove).

Terminal cross-section, fine-stranded: 1.5 mm²

Brand: Wieland Electric GmbH

Type: RST20I3C B 15

Part No.: 02.122.9100.0

gesis® crimp contact, female, 2.5 mm², with marking 1

System gesis® IP+ - Crimp contact, female, for circular connector RST20i3, with marking (groove).

Terminal cross-section, fine-stranded: 2.5 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I3C B 25

Part No.: 02.122.9200.0

gesis® crimp contact, female, 4.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST20i3, without marking (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Brand: Wieland Electric GmbH

Type: RST20I3C B 40

Part No.: 02.122.9300.0

gesis® crimp contact, male, 0.75 - 1.0 mm², with marking 1

System gesis® IP+ - Crimp contact, male, for circular connector RST20i3, with marking (groove).

Terminal cross-section, fine-stranded: 0.75 - 1.0 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I3C S 75 10

Part No.: 05.544.7800.0

gesis® crimp contact, male, 1.5 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST20i3, without marking (groove).

Terminal cross-section, fine-stranded: 1.5 mm²

Brand: Wieland Electric GmbH

Type: RST20I3C S 15

Part No.: 05.544.7900.0

gesis® crimp contact, male, 2.5 mm², with marking 1

System gesis® IP+ - Crimp contact, male, for circular connector RST20i3, with marking (groove).

Terminal cross-section, fine-stranded: 2.5 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I3C S 25

Part No.: 05.544.8000.0

gesis® crimp contact, male, 4.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST20i3, without marking (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Brand: Wieland Electric GmbH

Type: RST20I3C S 40

Part No.: 05.545.4600.0

Crimping tool - Crimping tool incl. system kit

Crimping tool - Crimping tool including system kit.

Brand: Wieland Electric GmbH

Part No.: 95.101.0800.0

Crimping tool - Crimping die B

Crimping tool - Crimping die B.

Brand: Wieland Electric GmbH

Part No.: 05.502.2100.0

Crimping tool - Contact positioner

Crimping tool - Contact positioner.

Brand: Wieland Electric GmbH

Part No.: 05.502.3600.0

Unlocking tool

Unlocking tool for crimp contacts.

Brand: Wieland Electric GmbH

Part No.: 05.502.3500.0

## Cable assemblies

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 15P x0SW

Part No.: 96.232.x000.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, green

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 15PH x0GN02

Part No.: 96.232.x001.7 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 15P x0SW

Part No.: 96.232.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, green

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 15PH x0GN02

Part No.: 96.232.x005.7 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 15P x0SW

Part No.: 96.232.x004.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, green

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 15PH x0GN02

Part No.: 96.232.x006.7 (x corresponds to length in m)

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 1.5 m, gray

System gesis® IP+ - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H05VV-F

Cable color: gray

Halogen-free: no

Length: 1.5 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15P 15GL

Part No.: 99.714.0000.7

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 2.5 m, gray

System gesis® IP+ - assembled H05VV-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding gray.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H05VV-F

Cable color: gray

Halogen-free: no

Length: 2.5 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15P 25GL

Part No.: 99.715.0000.7

### Cable assemblies, 1.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 15 x0SW

Part No.: 96.232.x030.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 3x 1.5 mm², 250 V, 16 A, length: x m, green

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 15H x0GN02

Part No.: 96.232.x031.7 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 15 x0SW

Part No.: 96.232.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, green

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 15H x0GN02

Part No.: 96.232.x035.7 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 15 x0SW

Part No.: 96.232.x034.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 1.5 mm², 250 V, 16 A, length: x m, green

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 1.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 15H x0GN02

Part No.: 96.232.x036.7 (x corresponds to length in m)

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 1.5 m, black

System gesis® IP+ - assembled H07RN-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 1.5 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15 15SW

Part No.: 99.712.0000.7

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 2.5 m, black

System gesis® IP+ - assembled H07RN-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 2.5 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15 25SW

Part No.: 99.713.0000.7

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 4.0 m, black

System gesis® IP+ - assembled H07RN-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 4.0 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15 40SW

Part No.: 99.716.0000.7

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 5,0 m, black

System gesis® IP+ - assembled H07RN-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 5,0 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15 50SW

Part No.: 99.718.0000.7

gesis® cable, female, SCHUKO-male, 3x 1.5 mm², 250 V, 16 A, length: 8,0 m, black

System gesis® IP+ - assembled H07RN-F cable with protective ground, 3-pole, 1.5 mm², female RST20i3 mit SCHUKO-male according to DIN 49441, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: 8,0 m

Brand: Wieland Electric GmbH

Type: RST20I3K1BI 15 80SW

Part No.: 99.717.0000.7

### Cable assemblies, 2.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 3x 2.5 mm², 250 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 25P x0SW

Part No.: 96.233.x000.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 3x 2.5 mm², 250 V, 20 A, length: x m, green

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 25PH x0GN02

Part No.: 96.233.x001.7 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 25P x0SW

Part No.: 96.233.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, green

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 25PH x0GN02

Part No.: 96.233.x005.7 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 25P x0SW

Part No.: 96.233.x004.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, green

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 25PH x0GN02

Part No.: 96.233.x006.7 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 3x 2.5 mm², 250 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 25 x0SW

Part No.: 96.233.x030.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 3x 2.5 mm², 250 V, 20 A, length: x m, green

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, female RST20i3, according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1BS 25H x0GN02

Part No.: 96.233.x031.7 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 25 x0SW

Part No.: 96.233.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, green

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², female RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1B 25H x0GN02

Part No.: 96.233.x035.7 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 25 x0SW

Part No.: 96.233.x034.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 3x 2.5 mm², 250 V, 20 A, length: x m, green

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 3-pole, 2.5 mm², with locking, male RST20i3, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding green.

Rated voltage: 250 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I3K1S 25H x0GN02

Part No.: 96.233.x036.7 (x corresponds to length in m)

# gesis® IP+ - Circular connector system IP66/68 - 4-pole - RST20i4

## Connector

## Cable diameter 6-10 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR1 GL

Part No.: 96.041.4053.0

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YR1 GL

Part No.: 96.043.4053.0

gesis® circular connector, IP66/68, splitter connector, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZRX GL

Part No.: 96.041.4253.0

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR1 SW

Part No.: 96.041.4053.1

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YR1 SW

Part No.: 96.043.4053.1

gesis® circular connector, IP66/68, splitter connector, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZRX SW

Part No.: 96.041.4253.1

gesis® circular connector, IP66/68, female, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR1S L BR01

Part No.: 96.041.4051.4

gesis® circular connector, IP66/68, female, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YR1S L BR01

Part No.: 96.043.4051.4

### Female with crimp connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 ZR1 V GL

Part No.: 96.141.0053.0

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 YR1 V GL

Part No.: 96.143.0053.0

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 ZR1 V SW

Part No.: 96.141.0053.1

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 YR1 V SW

Part No.: 96.143.0053.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR1 GL

Part No.: 96.042.4053.0

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YR1 GL

Part No.: 96.044.4053.0

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR1 SW

Part No.: 96.042.4053.1

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YR1 SW

Part No.: 96.044.4053.1

gesis® circular connector, IP66/68, male, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR1S L BR01

Part No.: 96.042.4051.4

gesis® circular connector, IP66/68, male, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YR1S L BR01

Part No.: 96.044.4051.4

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 ZR1 V GL

Part No.: 96.142.0053.0

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 YR1 V GL

Part No.: 96.144.0053.0

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 ZR1 V SW

Part No.: 96.142.0053.1

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 YR1 V SW

Part No.: 96.144.0053.1

## Cable diameter 10-14 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR2 GL

Part No.: 96.041.4153.0

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YR2 GL

Part No.: 96.043.4153.0

gesis® circular connector, IP66/68, splitter connector, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZRY GL

Part No.: 96.041.4353.0

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR2 SW

Part No.: 96.041.4153.1

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YR2 SW

Part No.: 96.043.4153.1

gesis® circular connector, IP66/68, splitter connector, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZRY SW

Part No.: 96.041.4353.1

### Female with crimp connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 ZR2 V GL

Part No.: 96.141.0153.0

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 YR2 V GL

Part No.: 96.143.0153.0

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 ZR2 V SW

Part No.: 96.141.0153.1

gesis® circular connector, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 YR2 V SW

Part No.: 96.143.0153.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR2 GL

Part No.: 96.042.4153.0

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YR2 GL

Part No.: 96.044.4153.0

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR2 SW

Part No.: 96.042.4153.1

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YR2 SW

Part No.: 96.044.4153.1

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 ZR2 V GL

Part No.: 96.142.0153.0

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 YR2 V GL

Part No.: 96.144.0153.0

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 ZR2 V SW

Part No.: 96.142.0153.1

gesis® circular connector, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 YR2 V SW

Part No.: 96.144.0153.1

## Cable diameter 13-18 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR3 GL

Part No.: 96.041.4553.0

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZR3 SW

Part No.: 96.041.4553.1

### Female with crimp connection

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 ZR3 V GL

Part No.: 96.141.4553.0

gesis® circular connector, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 ZR3 V SW

Part No.: 96.141.4553.1

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR3 GL

Part No.: 96.042.4553.0

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZR3 SW

Part No.: 96.042.4553.1

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 ZR3 V GL

Part No.: 96.142.4553.0

gesis® circular connector, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 ZR3 V SW

Part No.: 96.142.4553.1

## 1x AS-i profile cable

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 1x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZASSVL BR01

Part No.: 96.041.4951.4

gesis® circular connector, IP66/68, female, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 1x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YASSVL BR01

Part No.: 96.043.4951.4

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 1x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZASSVL BR01

Part No.: 96.042.4951.4

gesis® circular connector, IP66/68, male, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 1x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YASSVL BR01

Part No.: 96.044.4951.4

## 2x AS-i profile cable

### Female with screw connection

gesis® circular connector, IP66/68, female, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 2x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 ZASSVL BR01

Part No.: 96.041.4851.4

gesis® circular connector, IP66/68, female, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 2x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 YASSVL BR01

Part No.: 96.043.4851.4

### Male with screw connection

gesis® circular connector, IP66/68, male, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 2x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 ZASSVL BR01

Part No.: 96.042.4851.4

gesis® circular connector, IP66/68, male, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 4-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable: 2x AS-i profile cable

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 YASSVL BR01

Part No.: 96.044.4851.4

## Device connector

### M16

### Female with screw connection

gesis® device connector M16, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M03 GL

Part No.: 96.041.6153.0

gesis® device connector M16, IP66/68, female, 7° angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M13 GL

Part No.: 96.045.6153.0

gesis® device connector M16, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M03 SW

Part No.: 96.041.6153.1

gesis® device connector M16, IP66/68, female, 7° angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M13 SW

Part No.: 96.045.6153.1

gesis® device connector M16, IP66/68, female, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M03L BR01

Part No.: 96.041.6151.4

gesis® device connector M16, IP66/68, female, 7° angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M13L BR01

Part No.: 96.045.6151.4

### Female with crimp connection

gesis® device connector M16, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M03 GL

Part No.: 96.141.2153.0

gesis® device connector M16, IP66/68, female, 7° angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M13 GL

Part No.: 96.145.2153.0

gesis® device connector M16, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M03 SW

Part No.: 96.141.2153.1

gesis® device connector M16, IP66/68, female, 7° angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M13 SW

Part No.: 96.145.2153.1

### Male with screw connection

gesis® device connector M16, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M03 GL

Part No.: 96.042.6153.0

gesis® device connector M16, IP66/68, male, 7° angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M13 GL

Part No.: 96.046.6153.0

gesis® device connector M16, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M03 SW

Part No.: 96.042.6153.1

gesis® device connector M16, IP66/68, male, 7° angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M13 SW

Part No.: 96.046.6153.1

gesis® device connector M16, IP66/68, male, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M03L BR01

Part No.: 96.042.6151.4

gesis® device connector M16, IP66/68, male, 7° angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M13L BR01

Part No.: 96.046.6151.4

### Male with crimp connection,

gesis® device connector M16, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M03 GL

Part No.: 96.142.2153.0

gesis® device connector M16, IP66/68, male, 7° angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M13 GL

Part No.: 96.146.2153.0

gesis® device connector M16, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M03 SW

Part No.: 96.142.2153.1

gesis® device connector M16, IP66/68, male, 7° angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M13 SW

Part No.: 96.146.2153.1

### M20

### Female with screw connection

gesis® device connector M20, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M00 GL

Part No.: 96.041.6053.0

gesis® device connector M20, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M10 GL

Part No.: 96.043.6053.0

gesis® device connector M20, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M00 SW

Part No.: 96.041.6053.1

gesis® device connector M20, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M10 SW

Part No.: 96.043.6053.1

gesis® device connector M20, IP66/68, female, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M00L BR01

Part No.: 96.041.6051.4

gesis® device connector M20, IP66/68, female, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M10L BR01

Part No.: 96.043.6051.4

### Female with crimp connection

gesis® device connector M20, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M00 GL

Part No.: 96.141.2053.0

gesis® device connector M20, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M10 GL

Part No.: 96.143.2053.0

gesis® device connector M20, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M00 SW

Part No.: 96.141.2053.1

gesis® device connector M20, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M10 SW

Part No.: 96.143.2053.1

### Male with screw connection

gesis® device connector M20, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M00 GL

Part No.: 96.042.6053.0

gesis® device connector M20, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M10 GL

Part No.: 96.044.6053.0

gesis® device connector M20, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M00 SW

Part No.: 96.042.6053.1

gesis® device connector M20, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M10 SW

Part No.: 96.044.6053.1

gesis® device connector M20, IP66/68, male, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M00L BR01

Part No.: 96.042.6051.4

gesis® device connector M20, IP66/68, male, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M10L BR01

Part No.: 96.044.6051.4

### Male with crimp connection,

gesis® device connector M20, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M00 GL

Part No.: 96.142.2053.0

gesis® device connector M20, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M10 GL

Part No.: 96.144.2053.0

gesis® device connector M20, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M00 SW

Part No.: 96.142.2053.1

gesis® device connector M20, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M10 SW

Part No.: 96.144.2053.1

### M25

### Female with screw connection

gesis® device connector M25, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M01 GL

Part No.: 96.041.5053.0

gesis® device connector M25, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M11 GL

Part No.: 96.043.5053.0

gesis® device connector M25, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M01 SW

Part No.: 96.041.5053.1

gesis® device connector M25, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M11 SW

Part No.: 96.043.5053.1

gesis® device connector M25, IP66/68, female, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M01L BR01

Part No.: 96.041.5051.4

gesis® device connector M25, IP66/68, female, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S B1 M11L BR01

Part No.: 96.043.5051.4

### Female with crimp connection

gesis® device connector M25, IP66/68, female, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M01 GL

Part No.: 96.141.1053.0

gesis® device connector M25, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M11 GL

Part No.: 96.143.2253.0

gesis® device connector M25, IP66/68, female, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M01 SW

Part No.: 96.141.1053.1

gesis® device connector M25, IP66/68, female, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C B1 M11 SW

Part No.: 96.143.2253.1

### Male with screw connection

gesis® device connector M25, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M01 GL

Part No.: 96.042.5053.0

gesis® device connector M25, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M11 GL

Part No.: 96.044.5053.0

gesis® device connector M25, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M01 SW

Part No.: 96.042.5053.1

gesis® device connector M25, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M11 SW

Part No.: 96.044.5053.1

gesis® device connector M25, IP66/68, male, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M01L BR01

Part No.: 96.042.5051.4

gesis® device connector M25, IP66/68, male, angled, 4-pole, AS-i 24 V, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4S S1 M11L BR01

Part No.: 96.044.5051.4

### Male with crimp connection,

gesis® device connector M25, IP66/68, male, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M01 GL

Part No.: 96.142.1053.0

gesis® device connector M25, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M11 GL

Part No.: 96.144.2253.0

gesis® device connector M25, IP66/68, male, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M01 SW

Part No.: 96.142.1053.1

gesis® device connector M25, IP66/68, male, angled, 4-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 4-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking:  PE, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4C S1 M11 SW

Part No.: 96.144.2253.1

## Distribution block

gesis® compact distribution unit, IP66/68, 4-pole, 1 input, 3 outputs, 250/400 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to four M25 device connectors IP66/68, 4-pole, 1 input, 3 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Dimension: 104x162x57.2 mm

Brand: Wieland Electric GmbH

Type: RST20I4B 3P1 F VG SW

Part No.: 99.911.0000.7

gesis® multi distribution unit, IP66/68, 4-pole, 1 input, 4 outputs, 250/400 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to eight M25 device connectors IP66/68, 4-pole, 1 input, 4 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 4

Halogen-free: yes

Dimension: 104x162x96 mm

Brand: Wieland Electric GmbH

Type: RST20I4B 4P1 F VG SW

Part No.: 99.935.0000.7

gesis® multi distribution unit, IP66/68, 4-pole, 1 input, 5 outputs, 250/400 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to eight M25 device connectors IP66/68, 4-pole, 1 input, 5 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 5

Halogen-free: yes

Dimension: 104x162x96 mm

Brand: Wieland Electric GmbH

Type: RST20I4B 5P1 F VG SW

Part No.: 99.916.0000.7

gesis® multi distribution unit, IP66/68, 4-pole, 1 input, 7 outputs, 250/400 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to eight M25 device connectors IP66/68, 4-pole, 1 input, 7 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 7

Halogen-free: yes

Dimension: 104x162x96 mm

Brand: Wieland Electric GmbH

Type: RST20I4B 7P1 F VG SW

Part No.: 99.936.0000.7

## Accessories

gesis® Cover piece IP66/68 for male, 4-5-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS GL

Part No.: 99.531.0000.7

gesis® Cover piece IP66/68 for male, 4-5-pole, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS GL

Part No.: 05.565.9953.0

gesis® Cover piece IP66/68 for male, 4-5-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS SW

Part No.: 99.532.0000.7

gesis® Cover piece IP66/68 for male, 4-5-pole, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS SW

Part No.: 05.565.9953.1

gesis® Cover piece IP66/68 for female, 4-5-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS GL

Part No.: 99.529.0000.7

gesis® Cover piece IP66/68 for female, 4-5-pole, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS GL

Part No.: Z5.565.9853.0

gesis® Cover piece IP66/68 for female, 4-5-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS SW

Part No.: 99.530.0000.7

gesis® Cover piece IP66/68 for female, 4-5-pole, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I4 VS SW

Part No.: Z5.565.9853.1

gesis® Mounting plate for splitter connector, gray

System gesis® IP+ - Mounting plate for splitter connector RST20i4, gray.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG GR

Part No.: 01.006.1553.0

gesis® Mounting plate for splitter connector, black

System gesis® IP+ - Mounting plate for splitter connector RST20i4, black.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG SW

Part No.: 01.006.1553.1

gesis® crimp contact, female, 0.75 - 1.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST20i4, without marking (groove).

Terminal cross-section, fine-stranded: 0.75 - 1.0 mm²

Brand: Wieland Electric GmbH

Type: RST20I4C B 75 10

Part No.: 02.125.5521.8

gesis® crimp contact, female, 1.5 mm², with marking 1

System gesis® IP+ - Crimp contact, female, for circular connector RST20i4, with marking 1 (groove).

Terminal cross-section, fine-stranded: 1.5 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I4C B 15

Part No.: 02.125.5621.8

gesis® crimp contact, female, 2.5 mm², with marking 2

System gesis® IP+ - Crimp contact, female, for circular connector RST20i4, with marking 2 (groove).

Terminal cross-section, fine-stranded: 2.5 mm²

Marking: 2

Brand: Wieland Electric GmbH

Type: RST20I4C B 25

Part No.: 02.125.5721.8

gesis® crimp contact, female, 4.0 mm², with marking 3

System gesis® IP+ - Crimp contact, female, for circular connector RST20i4, with marking 3 (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Marking: 3

Brand: Wieland Electric GmbH

Type: RST20I4C B 40

Part No.: 02.125.5821.8

gesis® crimp contact, male, 0.75 - 1.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST20i4, without marking (groove).

Terminal cross-section, fine-stranded: 0.75 - 1.0 mm²

Brand: Wieland Electric GmbH

Type: RST20I4C S 75 10

Part No.: 05.545.0021.8

gesis® crimp contact, male, 1.5 mm², with marking 1

System gesis® IP+ - Crimp contact, male, for circular connector RST20i4, with marking 1 (groove).

Terminal cross-section, fine-stranded: 1.5 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I4C S 15

Part No.: 05.545.0121.8

gesis® crimp contact, male, 2.5 mm², with marking 2

System gesis® IP+ - Crimp contact, male, for circular connector RST20i4, with marking 2 (groove).

Terminal cross-section, fine-stranded: 2.5 mm²

Marking: 2

Brand: Wieland Electric GmbH

Type: RST20I4C S 25

Part No.: 05.545.0221.8

gesis® crimp contact, male, 4.0 mm², with marking 3

System gesis® IP+ - Crimp contact, male, for circular connector RST20i4, with marking 3 (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Marking: 3

Brand: Wieland Electric GmbH

Type: RST20I4C S 40

Part No.: 05.545.0321.8

Crimping tool - Crimping tool incl. system kit

Crimping tool - Crimping tool including system kit.

Brand: Wieland Electric GmbH

Part No.: 95.101.0800.0

Crimping tool - Crimping die B

Crimping tool - Crimping die B.

Brand: Wieland Electric GmbH

Part No.: 05.502.2100.0

Crimping tool - Contact positioner

Crimping tool - Contact positioner.

Brand: Wieland Electric GmbH

Part No.: 05.502.3600.0

Unlocking tool

Unlocking tool for crimp contacts.

Brand: Wieland Electric GmbH

Part No.: 05.502.3500.0

## Cable assemblies

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i4, female RST20i4, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1BS 15P x0SW

Part No.: 96.442.x000.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 4-pole, 1.5 mm², female RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1B 15P x0SW

Part No.: 96.442.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1S 15P x0SW

Part No.: 96.442.x004.1 (x corresponds to length in m)

### Cable assemblies, 1.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i4, female RST20i4, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1BS 15 x0SW

Part No.: 96.442.x030.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 4-pole, 1.5 mm², female RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1B 15 x0SW

Part No.: 96.442.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1S 15 x0SW

Part No.: 96.442.x034.1 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 4x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 4-pole, 2.5 mm², with locking, male RST20i4, female RST20i4, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1BS 25P x0SW

Part No.: 96.443.x000.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 4x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 4-pole, 2.5 mm², female RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1B 25P x0SW

Part No.: 96.443.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 4x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 4-pole, 2.5 mm², with locking, male RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1S 25P x0SW

Part No.: 96.443.x004.1 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 4x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 4-pole, 2.5 mm², with locking, male RST20i4, female RST20i4, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1BS 25 x0SW

Part No.: 96.443.x030.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 4x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 4-pole, 2.5 mm², female RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1B 25 x0SW

Part No.: 96.443.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 4x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 4-pole, 2.5 mm², with locking, male RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1S 25 x0SW

Part No.: 96.443.x034.1 (x corresponds to length in m)

### Cable assemblies, 1.5 mm², mains 4-pole, containing halogen

gesis® extension cable IP66/68, female, male, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled Ölflex Classic 110 extension cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i4, female RST20i4, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 110

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1BS 15P x0SW

Part No.: 96.442.x080.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled Ölflex Classic 110 connection cable with protective ground IP66/68, 4-pole, 1.5 mm², female RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 110

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1B 15P x0SW

Part No.: 96.442.x083.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 4x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled Ölflex Classic 110 connection cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 110

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1S 15P x0SW

Part No.: 96.442.x084.1 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², AS-i 24 V, 20 A, containing halogen

gesis® extension cable IP66/68, female, male, 4x 2.5 mm², AS-i 24 V, 20 A, length: x m, black

System gesis® IP+ - assembled PVC 4x 2.5 special compound extension cable with protective ground IP66/68, 4-pole, 2.5 mm², with locking, male RST20i4, female RST20i4, according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: PVC 4x 2.5 special compound

Cable color: brown

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1BS 15P x0SW

Part No.: 96.443.x082.4 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 4x 2.5 mm², AS-i 24 V, 20 A, length: x m, black

System gesis® IP+ - assembled PVC 4x 2.5 special compound connection cable with protective ground IP66/68, 4-pole, 2.5 mm², female RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: PVC 4x 2.5 special compound

Cable color: brown

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1B 15P x0SW

Part No.: 96.443.x087.4 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 4x 2.5 mm², AS-i 24 V, 20 A, length: x m, black

System gesis® IP+ - assembled PVC 4x 2.5 special compound connection cable with protective ground IP66/68, 4-pole, 2.5 mm², with locking, male RST20i4, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding brown.

Rated voltage: 24 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: PVC 4x 2.5 special compound

Cable color: brown

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I4K1S 15P x0SW

Part No.: 96.443.x088.4 (x corresponds to length in m)

# gesis® IP+ - Circular connector system IP66/68 - 5-pole - RST20i5

## Connector

## Cable diameter 6-10 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR1 GL

Part No.: 96.051.4053.0

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR1 GL

Part No.: 96.053.4053.0

gesis® circular connector, IP66/68, splitter connector, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRX GL

Part No.: 96.051.4253.0

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR1 SW

Part No.: 96.051.4053.1

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR1 SW

Part No.: 96.053.4053.1

gesis® circular connector, IP66/68, splitter connector, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRX SW

Part No.: 96.051.4253.1

gesis® circular connector, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR1SA TB04

Part No.: 96.051.4053.6

gesis® circular connector, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR1SA TB04

Part No.: 96.053.4053.6

gesis® circular connector, IP66/68, splitter connector, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRXSA TB04

Part No.: 96.051.4253.6

gesis® circular connector, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR1S L BR01

Part No.: 96.051.4051.4

gesis® circular connector, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR1S L BR01

Part No.: 96.053.4051.4

gesis® circular connector, IP66/68, splitter connector, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRXSL BR01

Part No.: 96.051.4251.4

gesis® circular connector, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR1S BL07

Part No.: 96.051.4053.9

gesis® circular connector, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR1S BL07

Part No.: 96.053.4053.9

### Female with crimp connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR1 V GL

Part No.: 96.151.0053.0

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR1 V GL

Part No.: 96.153.0053.0

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR1 V SW

Part No.: 96.151.0053.1

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR1 V SW

Part No.: 96.153.0053.1

gesis® circular connector, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR1SA TB04

Part No.: 96.151.0053.6

gesis® circular connector, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR1SA TB04

Part No.: 96.153.0053.6

gesis® circular connector, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR1S L BR01

Part No.: 96.151.0051.4

gesis® circular connector, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR1S L BR01

Part No.: 96.153.0051.4

gesis® circular connector, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR1S BL07

Part No.: 96.151.0053.9

gesis® circular connector, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR1S BL07

Part No.: 96.153.0053.9

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR1 GL

Part No.: 96.052.4053.0

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR1 GL

Part No.: 96.054.4053.0

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR1 SW

Part No.: 96.052.4053.1

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR1 SW

Part No.: 96.054.4053.1

gesis® circular connector, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR1SA TB04

Part No.: 96.052.4053.6

gesis® circular connector, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR1SA TB04

Part No.: 96.054.4053.6

gesis® circular connector, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR1S L BR01

Part No.: 96.052.4051.4

gesis® circular connector, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR1S L BR01

Part No.: 96.054.4051.4

gesis® circular connector, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR1S BL07

Part No.: 96.052.4053.9

gesis® circular connector, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR1S BL07

Part No.: 96.054.4053.9

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR1 V GL

Part No.: 96.152.0053.0

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR1 V GL

Part No.: 96.154.0053.0

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR1 V SW

Part No.: 96.152.0053.1

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR1 V SW

Part No.: 96.154.0053.1

gesis® circular connector, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR1SA TB04

Part No.: 96.152.0053.6

gesis® circular connector, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR1SA TB04

Part No.: 96.154.0053.6

gesis® circular connector, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR1S L BR01

Part No.: 96.152.0051.4

gesis® circular connector, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR1S L BR01

Part No.: 96.154.0051.4

gesis® circular connector, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR1S BL07

Part No.: 96.152.0053.9

gesis® circular connector, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 6.0 - 10.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR1S BL07

Part No.: 96.154.0053.9

## Cable diameter 10-14 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR2 GL

Part No.: 96.051.4153.0

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR2 GL

Part No.: 96.053.4153.0

gesis® circular connector, IP66/68, splitter connector, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRX GL

Part No.: 96.051.4353.0

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR2 SW

Part No.: 96.051.4153.1

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR2 SW

Part No.: 96.053.4153.1

gesis® circular connector, IP66/68, splitter connector, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRX SW

Part No.: 96.051.4353.1

gesis® circular connector, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR2SA TB04

Part No.: 96.051.4153.6

gesis® circular connector, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR2SA TB04

Part No.: 96.053.4153.6

gesis® circular connector, IP66/68, splitter connector, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRXSA TB04

Part No.: 96.051.4353.6

gesis® circular connector, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR2S L BR01

Part No.: 96.051.4151.4

gesis® circular connector, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR2S L BR01

Part No.: 96.053.4151.4

gesis® circular connector, IP66/68, splitter connector, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female with splitter connector (two cable glands), 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 1.5 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 2

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZRXSL BR01

Part No.: 96.051.4351.4

gesis® circular connector, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR2S BL07

Part No.: 96.051.4153.9

gesis® circular connector, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 YR2S BL07

Part No.: 96.053.4153.9

### Female with crimp connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR2 V GL

Part No.: 96.151.0153.0

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR2 V GL

Part No.: 96.153.0153.0

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR2 V SW

Part No.: 96.151.0153.1

gesis® circular connector, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR2 V SW

Part No.: 96.153.0153.1

gesis® circular connector, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR2SA TB04

Part No.: 96.151.0153.6

gesis® circular connector, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR2SA TB04

Part No.: 96.153.0153.6

gesis® circular connector, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR2S L BR01

Part No.: 96.151.0151.4

gesis® circular connector, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR2S L BR01

Part No.: 96.153.0151.4

gesis® circular connector, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR2S BL07

Part No.: 96.151.0153.9

gesis® circular connector, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 YR2S BL07

Part No.: 96.153.0153.9

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR2 GL

Part No.: 96.052.4153.0

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR2 GL

Part No.: 96.054.4153.0

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR2 SW

Part No.: 96.052.4153.1

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR2 SW

Part No.: 96.054.4153.1

gesis® circular connector, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR2SA TB04

Part No.: 96.052.4153.6

gesis® circular connector, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR2SA TB04

Part No.: 96.054.4153.6

gesis® circular connector, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR2S L BR01

Part No.: 96.052.4151.4

gesis® circular connector, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR2S L BR01

Part No.: 96.054.4151.4

gesis® circular connector, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR2S BL07

Part No.: 96.052.4153.9

gesis® circular connector, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 YR2S BL07

Part No.: 96.054.4153.9

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR2 V GL

Part No.: 96.152.0153.0

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR2 V GL

Part No.: 96.154.0153.0

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR2 V SW

Part No.: 96.152.0153.1

gesis® circular connector, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR2 V SW

Part No.: 96.154.0153.1

gesis® circular connector, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR2SA TB04

Part No.: 96.152.0153.6

gesis® circular connector, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR2SA TB04

Part No.: 96.154.0153.6

gesis® circular connector, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR2S L BR01

Part No.: 96.152.0151.4

gesis® circular connector, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR2S L BR01

Part No.: 96.154.0151.4

gesis® circular connector, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR2S BL07

Part No.: 96.152.0153.9

gesis® circular connector, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 90° angled, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 10.0 - 14.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 YR2S BL07

Part No.: 96.154.0153.9

## Cable diameter 13-18 mm

### Female with screw connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR3 GL

Part No.: 96.051.4553.0

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR3 SW

Part No.: 96.051.4553.1

gesis® circular connector, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR3SA TB04

Part No.: 96.051.4553.6

gesis® circular connector, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR3S L BR01

Part No.: 96.051.4551.4

gesis® circular connector, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 ZR3S BL07

Part No.: 96.051.4553.9

### Female with crimp connection

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR3 V GL

Part No.: 96.151.0553.0

gesis® circular connector, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR3 V SW

Part No.: 96.151.0553.1

gesis® circular connector, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR3SA TB04

Part No.: 96.151.0553.6

gesis® circular connector, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR3S L BR01

Part No.: 96.151.0551.4

gesis® circular connector, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, female, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 ZR3S BL07

Part No.: 96.151.0553.9

### Male with screw connection

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR3 GL

Part No.: 96.052.4553.0

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR3 SW

Part No.: 96.052.4553.1

gesis® circular connector, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR3SA TB04

Part No.: 96.052.4553.6

gesis® circular connector, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR3S L BR01

Part No.: 96.052.4551.4

gesis® circular connector, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with screw connection compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 ZR3S BL07

Part No.: 96.052.4553.9

### Male with crimp connection,

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR3 V GL

Part No.: 96.152.0553.0

gesis® circular connector, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR3 V SW

Part No.: 96.152.0553.1

gesis® circular connector, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR3SA TB04

Part No.: 96.152.0553.6

gesis® circular connector, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR3S L BR01

Part No.: 96.152.0551.4

gesis® circular connector, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Circular connector according to IEC 61535 for permanent installation with type of protection IP66/IP68, male with locking, 5-pole, turned contacts with crimp connection, compact housing with strain relief, field assembly, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Terminal cross-section: 0.75 - 4.0 mm²

Cable diameter: 13.0 - 18.0 mm (H05VV, H07RN-F)

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 ZR3S BL07

Part No.: 96.152.0553.9

## Device connector

### M16

### Female with screw connection

gesis® device connector M16, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M03 GL

Part No.: 96.051.6153.0

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M13 GL

Part No.: 96.055.6153.0

gesis® device connector M16, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M03 SW

Part No.: 96.051.6153.1

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M13 SW

Part No.: 96.055.6153.1

gesis® device connector M16, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M03A TB04

Part No.: 96.051.6153.6

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M13A TB04

Part No.: 96.055.6153.6

gesis® device connector M16, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M03L BR01

Part No.: 96.051.6151.4

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M13L BR01

Part No.: 96.055.6151.4

gesis® device connector M16, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M03 BL07

Part No.: 96.051.6153.9

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M13 BL07

Part No.: 96.055.6153.9

### Female with crimp connection

gesis® device connector M16, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M03 GL

Part No.: 96.151.2153.0

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M13 GL

Part No.: 96.155.2153.0

gesis® device connector M16, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M03 SW

Part No.: 96.151.2153.1

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M13 SW

Part No.: 96.155.2153.1

gesis® device connector M16, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M03A TB04

Part No.: 96.151.2153.6

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M13A TB04

Part No.: 96.155.2153.6

gesis® device connector M16, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M03L BR01

Part No.: 96.151.2151.4

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M13L BR01

Part No.: 96.155.2151.4

gesis® device connector M16, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M03 BL07

Part No.: 96.151.2153.9

gesis® device connector M16, IP66/68, female, 7° angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M13 BL07

Part No.: 96.155.2153.9

### Male with screw connection

gesis® device connector M16, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M03 GL

Part No.: 96.052.6153.0

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M13 GL

Part No.: 96.056.6153.0

gesis® device connector M16, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M03 SW

Part No.: 96.052.6153.1

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M13 SW

Part No.: 96.056.6153.1

gesis® device connector M16, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M03A TB04

Part No.: 96.052.6153.6

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M13A TB04

Part No.: 96.056.6153.6

gesis® device connector M16, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M03L BR01

Part No.: 96.052.6151.4

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M13L BR01

Part No.: 96.056.6151.4

gesis® device connector M16, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M03 BL07

Part No.: 96.052.6153.9

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M13 BL07

Part No.: 96.056.6153.9

### Male with crimp connection,

gesis® device connector M16, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M03 GL

Part No.: 96.152.2153.0

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M13 GL

Part No.: 96.156.2153.0

gesis® device connector M16, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M03 SW

Part No.: 96.152.2153.1

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M13 SW

Part No.: 96.156.2153.1

gesis® device connector M16, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M03A TB04

Part No.: 96.152.2153.6

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M13A TB04

Part No.: 96.156.2153.6

gesis® device connector M16, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M03L BR01

Part No.: 96.152.2151.4

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M13L BR01

Part No.: 96.156.2151.4

gesis® device connector M16, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M03 BL07

Part No.: 96.152.2153.9

gesis® device connector M16, IP66/68, male, 7° angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 7° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M16x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M13 BL07

Part No.: 96.156.2153.9

### M20

### Female with screw connection

gesis® device connector M20, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M00 GL

Part No.: 96.051.6053.0

gesis® device connector M20, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M10 GL

Part No.: 96.053.6053.0

gesis® device connector M20, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M00 SW

Part No.: 96.051.6053.1

gesis® device connector M20, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M10 SW

Part No.: 96.053.6053.1

gesis® device connector M20, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M00A TB04

Part No.: 96.051.6053.6

gesis® device connector M20, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M10A TB04

Part No.: 96.053.6053.6

gesis® device connector M20, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M00L BR01

Part No.: 96.051.6051.4

gesis® device connector M20, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M10L BR01

Part No.: 96.053.6051.4

gesis® device connector M20, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M00 BL07

Part No.: 96.051.6053.9

gesis® device connector M20, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M10 BL07

Part No.: 96.053.6053.9

### Female with crimp connection

gesis® device connector M20, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M00 GL

Part No.: 96.151.2053.0

gesis® device connector M20, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M10 GL

Part No.: 96.153.2053.0

gesis® device connector M20, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M00 SW

Part No.: 96.151.2053.1

gesis® device connector M20, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M10 SW

Part No.: 96.153.2053.1

gesis® device connector M20, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M00A TB04

Part No.: 96.151.2053.6

gesis® device connector M20, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M10A TB04

Part No.: 96.153.2053.6

gesis® device connector M20, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M00L BR01

Part No.: 96.151.2051.4

gesis® device connector M20, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M10L BR01

Part No.: 96.153.2051.4

gesis® device connector M20, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M00 BL07

Part No.: 96.151.2053.9

gesis® device connector M20, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M10 BL07

Part No.: 96.153.2053.9

### Male with screw connection

gesis® device connector M20, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M00 GL

Part No.: 96.052.6053.0

gesis® device connector M20, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M10 GL

Part No.: 96.054.6053.0

gesis® device connector M20, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M00 SW

Part No.: 96.052.6053.1

gesis® device connector M20, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M10 SW

Part No.: 96.054.6053.1

gesis® device connector M20, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M00A TB04

Part No.: 96.052.6053.6

gesis® device connector M20, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M10A TB04

Part No.: 96.054.6053.6

gesis® device connector M20, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M00L BR01

Part No.: 96.052.6051.4

gesis® device connector M20, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M10L BR01

Part No.: 96.054.6051.4

gesis® device connector M20, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M00 BL07

Part No.: 96.052.6053.9

gesis® device connector M20, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M10 BL07

Part No.: 96.054.6053.9

### Male with crimp connection,

gesis® device connector M20, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M00 GL

Part No.: 96.152.2053.0

gesis® device connector M20, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M10 GL

Part No.: 96.154.2053.0

gesis® device connector M20, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M00 SW

Part No.: 96.152.2053.1

gesis® device connector M20, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M10 SW

Part No.: 96.154.2053.1

gesis® device connector M20, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M00A TB04

Part No.: 96.152.2053.6

gesis® device connector M20, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M10A TB04

Part No.: 96.154.2053.6

gesis® device connector M20, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M00L BR01

Part No.: 96.152.2051.4

gesis® device connector M20, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M10L BR01

Part No.: 96.154.2051.4

gesis® device connector M20, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M00 BL07

Part No.: 96.152.2053.9

gesis® device connector M20, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M20x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M10 BL07

Part No.: 96.154.2053.9

### M25

### Female with screw connection

gesis® device connector M25, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M02 GL

Part No.: 96.051.5053.0

gesis® device connector M25, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M12 GL

Part No.: 96.053.6253.0

gesis® device connector M25, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M02 SW

Part No.: 96.051.5053.1

gesis® device connector M25, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M12 SW

Part No.: 96.053.6253.1

gesis® device connector M25, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M02A TB04

Part No.: 96.051.5053.6

gesis® device connector M25, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M12A TB04

Part No.: 96.053.6253.6

gesis® device connector M25, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M02L BR01

Part No.: 96.051.5051.4

gesis® device connector M25, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M12L BR01

Part No.: 96.053.6251.4

gesis® device connector M25, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M02 BL07

Part No.: 96.051.5053.9

gesis® device connector M25, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S B1 M12 BL07

Part No.: 96.053.6253.9

### Female with crimp connection

gesis® device connector M25, IP66/68, female, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M02 GL

Part No.: 96.151.1053.0

gesis® device connector M25, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M12 GL

Part No.: 96.153.2253.0

gesis® device connector M25, IP66/68, female, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M02 SW

Part No.: 96.151.1053.1

gesis® device connector M25, IP66/68, female, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, N, PE

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M12 SW

Part No.: 96.153.2253.1

gesis® device connector M25, IP66/68, female, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M02A TB04

Part No.: 96.151.1053.6

gesis® device connector M25, IP66/68, female, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: L, PE, N, D1, D2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M12A TB04

Part No.: 96.153.2253.6

gesis® device connector M25, IP66/68, female, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M02L BR01

Part No.: 96.151.1051.4

gesis® device connector M25, IP66/68, female, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M12L BR01

Part No.: 96.153.2251.4

gesis® device connector M25, IP66/68, female, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M02 BL07

Part No.: 96.151.1053.9

gesis® device connector M25, IP66/68, female, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, female, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 1, 2, 3, 4, 5

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C B1 M12 BL07

Part No.: 96.153.2253.9

### Male with screw connection

gesis® device connector M25, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M02 GL

Part No.: 96.052.5053.0

gesis® device connector M25, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M12 GL

Part No.: 96.054.6253.0

gesis® device connector M25, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M02 SW

Part No.: 96.052.5053.1

gesis® device connector M25, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M12 SW

Part No.: 96.054.6253.1

gesis® device connector M25, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M02A TB04

Part No.: 96.052.5053.6

gesis® device connector M25, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M12A TB04

Part No.: 96.054.6253.6

gesis® device connector M25, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M02L BR01

Part No.: 96.052.5051.4

gesis® device connector M25, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M12L BR01

Part No.: 96.054.6251.4

gesis® device connector M25, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M02 BL07

Part No.: 96.052.5053.9

gesis® device connector M25, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with screw connection fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5S S1 M12 BL07

Part No.: 96.054.6253.9

### Male with crimp connection,

gesis® device connector M25, IP66/68, male, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M02 GL

Part No.: 96.152.1053.0

gesis® device connector M25, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, gray

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding gray.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M12 GL

Part No.: 96.154.2253.0

gesis® device connector M25, IP66/68, male, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M02 SW

Part No.: 96.152.1053.1

gesis® device connector M25, IP66/68, male, angled, 5-pole, 250/400 V, 20 A, black

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section, fine-stranded: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: PE, N, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M12 SW

Part No.: 96.154.2253.1

gesis® device connector M25, IP66/68, male, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M02A TB04

Part No.: 96.152.1053.6

gesis® device connector M25, IP66/68, male, angled, 5-pole, 250 V + dimming, turquoise

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: D2, D1, N, PE, L

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M12A TB04

Part No.: 96.154.2253.6

gesis® device connector M25, IP66/68, male, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M02L BR01

Part No.: 96.152.1051.4

gesis® device connector M25, IP66/68, male, angled, 5-pole, low voltage, brown

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding brown.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M12L BR01

Part No.: 96.154.2251.4

gesis® device connector M25, IP66/68, male, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M02 BL07

Part No.: 96.152.1053.9

gesis® device connector M25, IP66/68, male, angled, 5-pole, switching functionality, 250 V, blue

System gesis® IP+ - Device connector according to IEC 61535 for permanent installation, male with locking, 5-pole, 90° angled, turned contacts with crimp connection, fastening screw from inside, mechanical/color coding blue.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: up to IP66/IP68 (3 m, 2 h)

Thread: M25x1.5

Terminal cross-section: 0.75 - 4.0 mm²

Housing material: PA66, V2

Sealing material: NBR

Connections per pole: 1

Marking: 5, 4, 3, 2, 1

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5C S1 M12 BL07

Part No.: 96.154.2253.9

## Distribution block

gesis® compact distribution unit, IP66/68, 5-pole, 1 input, 3 outputs, 250/400 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to four M25 device connectors IP66/68, 5-pole, 1 input, 3 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 3

Halogen-free: yes

Dimension: 104x162x57.2 mm

Brand: Wieland Electric GmbH

Type: RST20I5B 3P1 F VG SW

Part No.: 96.050.0153.1

gesis® multi distribution unit, IP66/68, 5-pole, 1 input, 5 outputs, 250/400 V, 20 A, black

System gesis® IP+ - Distribution unit for circular connector IP66/68 according to IEC 61535, distribution unit for optional mounting of up to eight M25 device connectors IP66/68, 5-pole, 1 input, 5 outputs, ready wired, halogen-free wires with 2.5 mm².

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Housing material: PA66, V2

Sealing material: NBR

Input: 1

Outputs: 5

Halogen-free: yes

Dimension: 104x162x96 mm

Brand: Wieland Electric GmbH

Type: RST20I5B 5P1 F VG SW

Part No.: 96.050.2153.1

## Accessories

gesis® Cover piece IP66/68 for male, 4-5-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS GL

Part No.: 99.531.0000.7

gesis® Cover piece IP66/68 for male, 4-5-pole, gray

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS GL

Part No.: 05.565.9953.0

gesis® Cover piece IP66/68 for male, 4-5-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS SW

Part No.: 99.532.0000.7

gesis® Cover piece IP66/68 for male, 4-5-pole, black

System gesis® IP+ - Cover piece IP66/68 for male parts RST20i4 and RST20i5, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS SW

Part No.: 05.565.9953.1

gesis® Cover piece IP66/68 for female, 4-5-pole, captive against loss, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, captive against loss, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS GL

Part No.: 99.529.0000.7

gesis® Cover piece IP66/68 for female, 4-5-pole, gray

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, gray.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS GL

Part No.: Z5.565.9853.0

gesis® Cover piece IP66/68 for female, 4-5-pole, captive against loss, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, captive against loss, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS SW

Part No.: 99.530.0000.7

gesis® Cover piece IP66/68 for female, 4-5-pole, black

System gesis® IP+ - Cover piece IP66/68 for female parts RST20i4 and RST20i5, with locking, black.

Housing material: PA66, V2

Sealing material: NBR

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST20I5 VS SW

Part No.: Z5.565.9853.1

gesis® Mounting plate for splitter connector, gray

System gesis® IP+ - Mounting plate for splitter connector RST20i4, gray.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG GR

Part No.: 01.006.1553.0

gesis® Mounting plate for splitter connector, black

System gesis® IP+ - Mounting plate for splitter connector RST20i4, black.

Housing material: PA66, V2

Halogen-free: yes

Brand: Wieland Electric GmbH

Type: RST DOPPELABGANG SW

Part No.: 01.006.1553.1

gesis® crimp contact, female, 0.75 - 1.0 mm², without marking

System gesis® IP+ - Crimp contact, female, for circular connector RST20i5, without marking (groove).

Terminal cross-section, fine-stranded: 0.75 - 1.0 mm²

Brand: Wieland Electric GmbH

Type: RST20I5C B 75 10

Part No.: 02.125.5521.8

gesis® crimp contact, female, 1.5 mm², with marking 1

System gesis® IP+ - Crimp contact, female, for circular connector RST20i5, with marking 1 (groove).

Terminal cross-section, fine-stranded: 1.5 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I5C B 15

Part No.: 02.125.5621.8

gesis® crimp contact, female, 2.5 mm², with marking 2

System gesis® IP+ - Crimp contact, female, for circular connector RST20i5, with marking 2 (groove).

Terminal cross-section, fine-stranded: 2.5 mm²

Marking: 2

Brand: Wieland Electric GmbH

Type: RST20I5C B 25

Part No.: 02.125.5721.8

gesis® crimp contact, female, 4.0 mm², with marking 3

System gesis® IP+ - Crimp contact, female, for circular connector RST20i5, with marking 3 (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Marking: 3

Brand: Wieland Electric GmbH

Type: RST20I5C B 40

Part No.: 02.125.5821.8

gesis® crimp contact, male, 0.75 - 1.0 mm², without marking

System gesis® IP+ - Crimp contact, male, for circular connector RST20i5, without marking (groove).

Terminal cross-section, fine-stranded: 0.75 - 1.0 mm²

Brand: Wieland Electric GmbH

Type: RST20I5C S 75 10

Part No.: 05.545.0021.8

gesis® crimp contact, male, 1.5 mm², with marking 1

System gesis® IP+ - Crimp contact, male, for circular connector RST20i5, with marking 1 (groove).

Terminal cross-section, fine-stranded: 1.5 mm²

Marking: 1

Brand: Wieland Electric GmbH

Type: RST20I5C S 15

Part No.: 05.545.0121.8

gesis® crimp contact, male, 2.5 mm², with marking 2

System gesis® IP+ - Crimp contact, male, for circular connector RST20i5, with marking 2 (groove).

Terminal cross-section, fine-stranded: 2.5 mm²

Marking: 2

Brand: Wieland Electric GmbH

Type: RST20I5C S 25

Part No.: 05.545.0221.8

gesis® crimp contact, male, 4.0 mm², with marking 3

System gesis® IP+ - Crimp contact, male, for circular connector RST20i5, with marking 3 (groove).

Terminal cross-section, fine-stranded: 4.0 mm²

Marking: 3

Brand: Wieland Electric GmbH

Type: RST20I5C S 40

Part No.: 05.545.0321.8

Crimping tool - Crimping tool incl. system kit

Crimping tool - Crimping tool including system kit.

Brand: Wieland Electric GmbH

Part No.: 95.101.0800.0

Crimping tool - Crimping die B

Crimping tool - Crimping die B.

Brand: Wieland Electric GmbH

Part No.: 05.502.2100.0

Crimping tool - Contact positioner

Crimping tool - Contact positioner.

Brand: Wieland Electric GmbH

Part No.: 05.502.3600.0

Unlocking tool

Unlocking tool for crimp contacts.

Brand: Wieland Electric GmbH

Part No.: 05.502.3500.0

## Cable assemblies

### Cable assemblies, 1.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 15P x0SW

Part No.: 96.452.x000.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 5x 1.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 15PH x0TB04

Part No.: 96.452.x000.6 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 15P x0SW

Part No.: 96.452.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 1.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 15PH x0TB04

Part No.: 96.452.x003.6 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 15P x0SW

Part No.: 96.452.x004.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 1.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 15PH x0TB04

Part No.: 96.452.x004.6 (x corresponds to length in m)

### Cable assemblies, 1.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 15 x0SW

Part No.: 96.452.x030.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 5x 1.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 15H x0TB04

Part No.: 96.452.x030.6 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 15 x0SW

Part No.: 96.452.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 1.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 15H x0TB04

Part No.: 96.452.x033.6 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 1.5 mm², 250/400 V, 16 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 15 x0SW

Part No.: 96.452.x034.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 1.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 1.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 16 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 15H x0TB04

Part No.: 96.452.x034.6 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², containing halogen

gesis® extension cable IP66/68, female, male, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 25P x0SW

Part No.: 96.453.x000.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 5x 2.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 25PH x0TB04

Part No.: 96.453.x000.6 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 25P x0SW

Part No.: 96.453.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 2.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 25PH x0TB04

Part No.: 96.453.x003.6 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 25P x0SW

Part No.: 96.453.x004.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 2.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 25PH x0TB04

Part No.: 96.453.x004.6 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 25 x0SW

Part No.: 96.453.x030.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 5x 2.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 25H x0TB04

Part No.: 96.453.x030.6 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 25 x0SW

Part No.: 96.453.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 2.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 25H x0TB04

Part No.: 96.453.x033.6 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 25 x0SW

Part No.: 96.453.x034.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 2.5 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 2.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 25H x0TB04

Part No.: 96.453.x034.6 (x corresponds to length in m)

### Cable assemblies, 4.0 mm², containing halogen

gesis® extension cable IP66/68, female, male, 5x 4.0 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 40P x0SW

Part No.: 96.454.x000.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 5x 4.0 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F extension cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 40PH x0TB04

Part No.: 96.454.x000.6 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 4.0 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 40P x0SW

Part No.: 96.454.x003.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 4.0 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 40PH x0TB04

Part No.: 96.454.x003.6 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 4.0 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 40P x0SW

Part No.: 96.454.x004.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 4.0 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H05VV-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H05VV-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 40PH x0TB04

Part No.: 96.454.x004.6 (x corresponds to length in m)

### Cable assemblies, 4.0 mm², insulating rubber compound

gesis® extension cable IP66/68, female, male, 5x 4.0 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 40 x0SW

Part No.: 96.454.x030.1 (x corresponds to length in m)

gesis® extension cable IP66/68, female, male, 5x 4.0 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F extension cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 40H x0TB04

Part No.: 96.454.x030.6 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 4.0 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 40 x0SW

Part No.: 96.454.x033.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 4.0 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 40H x0TB04

Part No.: 96.454.x033.6 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 4.0 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 40 x0SW

Part No.: 96.454.x034.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 4.0 mm², 250 V + dimming, length: x m, turquoise

System gesis® IP+ - assembled H07RN-F connection cable with protective ground IP66/68, 5-pole, 4.0 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical/color coding turquoise.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: H07RN-F

Cable color: black

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 40H x0TB04

Part No.: 96.454.x034.6 (x corresponds to length in m)

### Cable assemblies, 2.5 mm², 20 A, mains 5-pole, containing halogen

gesis® extension cable IP66/68, female, male, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled Ölflex Classic 110 extension cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i5, female RST20i5, according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 110

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1BS 25P x0SW

Part No.: 96.453.x080.1 (x corresponds to length in m)

gesis® connection cable IP66/68, female, free end, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled Ölflex Classic 110 connection cable with protective ground IP66/68, 4-pole, 1.5 mm², female RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 110

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1B 25P x0SW

Part No.: 96.453.x083.1 (x corresponds to length in m)

gesis® connection cable IP66/68, male, free end, 5x 2.5 mm², 250/400 V, 20 A, length: x m, black

System gesis® IP+ - assembled Ölflex Classic 110 connection cable with protective ground IP66/68, 4-pole, 1.5 mm², with locking, male RST20i5, free end (ultrasonic welded), according to IEC 61535, mechanical coding gray/black, color coding black.

Rated voltage: 250/400 V

Rated current: 20 A

Rated impulse voltage: 4 kV

Type of protection: IP66/IP68 (3 m, 2 h)

Cable type: Ölflex Classic 110

Cable color: gray

Halogen-free: no

Length: x m

Brand: Wieland Electric GmbH

Type: RST20I5K1S 25P x0SW

Part No.: 96.453.x084.1 (x corresponds to length in m)

01.006.1553.0	96, 233, 309, 414

01.006.1553.1	97, 234, 310, 415

02.122.9000.0	234

02.122.9100.0	234

02.122.9200.0	234

02.122.9300.0	234

02.125.5521.8	310, 415

02.125.5621.8	310, 415

02.125.5721.8	310, 415

02.125.5821.8	310, 415

05.502.2100.0	235, 311, 416

05.502.3500.0	236, 312, 417

05.502.3600.0	235, 311, 416

05.544.7800.0	235

05.544.7900.0	235

05.544.8000.0	235

05.545.0021.8	311, 416

05.545.0121.8	311, 416

05.545.0221.8	311, 416

05.545.0321.8	311, 416

05.545.4600.0	235

05.564.4453.0	95, 232, 308, 413

05.564.4453.1	95, 232

05.565.9953.1	308, 413

95.101.0800.0	235, 311, 416

96.020.0150.8	93

96.020.0151.4	91

96.020.0153.0	90

96.020.0153.1	91

96.020.0250.8	93

96.020.0251.4	92

96.020.0253.0	90

96.020.0253.1	91

96.021.0050.8	8

96.021.0051.4	6

96.021.0053.0	4

96.021.0053.1	5

96.021.0151.4	24

96.021.0153.0	22

96.021.0153.1	23

96.021.0250.8	9

96.021.0251.4	7

96.021.0253.0	5

96.021.0253.1	6

96.021.0351.4	25

96.021.0353.0	23

96.021.0353.1	24

96.021.0453.0	36

96.021.0453.1	37

96.021.0950.8	45

96.021.0951.4	44

96.021.1050.8	78

96.021.1051.4	78

96.021.1053.0	76

96.021.1053.1	77

96.021.2051.4	66

96.021.2053.0	64

96.021.2053.1	65

96.021.2150.8	54

96.021.2151.4	54

96.021.2153.0	52

96.021.2153.1	53

96.021.4050.8	13

96.021.4051.4	12

96.021.4053.0	10

96.021.4053.1	11

96.021.4151.4	28

96.021.4153.0	26

96.021.4153.1	27

96.021.4250.8	14

96.021.4251.4	13

96.021.4253.0	11

96.021.4253.1	12

96.021.4351.4	29

96.021.4353.0	27

96.021.4353.1	28

96.021.4453.0	38

96.021.4453.1	39

96.021.4950.8	47

96.021.4951.4	46

96.021.5050.8	82

96.021.5051.4	81

96.021.5053.0	80

96.021.5053.1	81

96.021.6050.8	69

96.021.6051.4	68

96.021.6053.0	67

96.021.6053.1	68

96.021.6150.8	57

96.021.6151.4	56

96.021.6153.0	55

96.021.6153.1	56

96.022.0050.8	17

96.022.0051.4	17

96.022.0053.0	15

96.022.0053.1	16

96.022.0151.4	32

96.022.0153.0	30

96.022.0153.1	31

96.022.0453.0	40

96.022.0453.1	41

96.022.0950.8	49

96.022.0951.4	48

96.022.1050.8	85

96.022.1051.4	85

96.022.1053.0	83

96.022.1053.1	84

96.022.2051.4	72

96.022.2053.0	70

96.022.2053.1	71

96.022.2150.8	60

96.022.2151.4	60

96.022.2153.0	58

96.022.2153.1	59

96.022.4050.8	21

96.022.4051.4	20

96.022.4053.0	19

96.022.4053.1	20

96.022.4151.4	34

96.022.4153.0	33

96.022.4153.1	34

96.022.4453.0	42

96.022.4453.1	43

96.022.4950.8	51

96.022.4951.4	50

96.022.5050.8	89

96.022.5051.4	88

96.022.5053.0	87

96.022.5053.1	88

96.022.6050.8	75

96.022.6051.4	74

96.022.6053.0	73

96.022.6053.1	74

96.022.6150.8	63

96.022.6151.4	62

96.022.6153.0	61

96.022.6153.1	62

96.023.0050.8	8

96.023.0051.4	7

96.023.0053.0	4

96.023.0053.1	6

96.023.0151.4	25

96.023.0153.0	22

96.023.0153.1	24

96.023.0453.0	36

96.023.0453.1	37

96.023.0950.8	45

96.023.0951.4	44

96.023.1050.8	79

96.023.1051.4	78

96.023.1053.0	76

96.023.1053.1	77

96.023.2050.8	66

96.023.2051.4	66

96.023.2053.0	64

96.023.2053.1	65

96.023.4050.8	14

96.023.4051.4	13

96.023.4053.0	10

96.023.4053.1	11

96.023.4151.4	29

96.023.4153.0	26

96.023.4153.1	27

96.023.4453.0	38

96.023.4453.1	39

96.023.4950.8	47

96.023.4951.4	46

96.023.5050.8	82

96.023.5051.4	82

96.023.5053.0	80

96.023.5053.1	81

96.023.6050.8	69

96.023.6051.4	69

96.023.6053.0	67

96.023.6053.1	68

96.024.0050.8	18

96.024.0051.4	17

96.024.0053.0	15

96.024.0053.1	16

96.024.0151.4	32

96.024.0153.0	30

96.024.0153.1	31

96.024.0453.0	40

96.024.0453.1	41

96.024.0950.8	49

96.024.0951.4	48

96.024.1050.8	86

96.024.1051.4	85

96.024.1053.0	83

96.024.1053.1	84

96.024.2050.8	72

96.024.2051.4	72

96.024.2053.0	70

96.024.2053.1	71

96.024.4050.8	21

96.024.4051.4	21

96.024.4053.0	19

96.024.4053.1	20

96.024.4151.4	35

96.024.4153.0	33

96.024.4153.1	34

96.024.4453.0	42

96.024.4453.1	43

96.024.4950.8	51

96.024.4951.4	50

96.024.5050.8	89

96.024.5051.4	89

96.024.5053.0	87

96.024.5053.1	88

96.024.6050.8	75

96.024.6051.4	75

96.024.6053.0	73

96.024.6053.1	74

96.025.2151.4	54

96.025.2153.0	52

96.025.2153.1	53

96.025.6150.8	57

96.025.6151.4	57

96.025.6153.0	55

96.025.6153.1	56

96.026.2151.4	60

96.026.2153.0	58

96.026.2153.1	59

96.026.6150.8	63

96.026.6151.4	63

96.026.6153.0	61

96.026.6153.1	62

96.030.0151.4	230

96.030.0153.0	228

96.030.0153.1	229

96.030.0155.7	229

96.030.0251.4	230

96.030.0253.0	228

96.030.0253.1	229

96.030.0255.7	230

96.031.0051.4	112

96.031.0053.0	108

96.031.0053.1	109

96.031.0053.9	113

96.031.0055.7	110

96.031.0151.4	136

96.031.0153.0	132

96.031.0153.1	133

96.031.0153.9	136

96.031.0155.7	134

96.031.0253.0	109

96.031.0253.1	110

96.031.0255.7	111

96.031.0353.0	133

96.031.0353.1	134

96.031.0355.7	135

96.031.1051.4	208

96.031.1053.0	206

96.031.1053.1	207

96.031.1053.9	209

96.031.1055.7	208

96.031.2051.4	186

96.031.2053.0	184

96.031.2053.1	185

96.031.2053.9	187

96.031.2055.7	186

96.031.2151.4	164

96.031.2153.0	162

96.031.2153.1	163

96.031.2153.9	165

96.031.2155.7	164

96.031.4051.4	117

96.031.4053.0	114

96.031.4053.1	115

96.031.4053.9	118

96.031.4055.7	116

96.031.4151.4	141

96.031.4153.0	138

96.031.4153.1	139

96.031.4153.9	142

96.031.4155.7	140

96.031.4253.0	115

96.031.4253.1	116

96.031.4255.7	117

96.031.4353.0	139

96.031.4353.1	140

96.031.4355.7	141

96.031.4553.0	156

96.031.4553.1	156

96.031.4555.7	157

96.031.5051.4	213

96.031.5053.0	211

96.031.5053.1	212

96.031.5053.9	214

96.031.5055.7	212

96.031.6051.4	191

96.031.6053.0	189

96.031.6053.1	190

96.031.6053.9	192

96.031.6055.7	190

96.031.6151.4	169

96.031.6153.0	167

96.031.6153.1	168

96.031.6153.9	170

96.031.6155.7	168

96.032.0051.4	123

96.032.0053.0	121

96.032.0053.1	122

96.032.0053.9	124

96.032.0055.7	123

96.032.0151.4	147

96.032.0153.0	145

96.032.0153.1	146

96.032.0153.9	148

96.032.0155.7	147

96.032.1051.4	219

96.032.1053.0	217

96.032.1053.1	218

96.032.1053.9	220

96.032.1055.7	219

96.032.2051.4	197

96.032.2053.0	195

96.032.2053.1	196

96.032.2053.9	198

96.032.2055.7	197

96.032.2151.4	175

96.032.2153.0	173

96.032.2153.1	174

96.032.2153.9	176

96.032.2155.7	175

96.032.4051.4	128

96.032.4053.0	126

96.032.4053.1	127

96.032.4053.9	129

96.032.4055.7	127

96.032.4151.4	152

96.032.4153.0	150

96.032.4153.1	151

96.032.4153.9	153

96.032.4155.7	151

96.032.4553.0	159

96.032.4553.1	159

96.032.4555.7	160

96.032.5051.4	224

96.032.5053.0	222

96.032.5053.1	223

96.032.5053.9	225

96.032.5055.7	223

96.032.6051.4	202

96.032.6053.0	200

96.032.6053.1	201

96.032.6053.9	203

96.032.6055.7	201

96.032.6151.4	180

96.032.6153.0	178

96.032.6153.1	179

96.032.6153.9	181

96.032.6155.7	179

96.033.0051.4	112

96.033.0053.0	108

96.033.0053.1	110

96.033.0053.9	113

96.033.0055.7	111

96.033.0151.4	136

96.033.0153.0	132

96.033.0153.1	134

96.033.0153.9	137

96.033.0155.7	135

96.033.1051.4	209

96.033.1053.0	206

96.033.1053.1	207

96.033.1053.9	210

96.033.1055.7	208

96.033.2051.4	187

96.033.2053.0	184

96.033.2053.1	185

96.033.2053.9	188

96.033.2055.7	186

96.033.4051.4	118

96.033.4053.0	114

96.033.4053.1	115

96.033.4053.9	118

96.033.4055.7	117

96.033.4151.4	142

96.033.4153.0	138

96.033.4153.1	139

96.033.4153.9	142

96.033.4155.7	141

96.033.5051.4	213

96.033.5053.0	211

96.033.5053.1	212

96.033.5053.9	214

96.033.5055.7	213

96.033.6051.4	191

96.033.6053.0	189

96.033.6053.1	190

96.033.6053.9	192

96.033.6055.7	191

96.034.0051.4	124

96.034.0053.0	121

96.034.0053.1	122

96.034.0053.9	125

96.034.0055.7	123

96.034.0151.4	148

96.034.0153.0	145

96.034.0153.1	146

96.034.0153.9	149

96.034.0155.7	147

96.034.1051.4	220

96.034.1053.0	217

96.034.1053.1	218

96.034.1053.9	221

96.034.1055.7	219

96.034.2051.4	198

96.034.2053.0	195

96.034.2053.1	196

96.034.2053.9	199

96.034.2055.7	197

96.034.4051.4	128

96.034.4053.0	126

96.034.4053.1	127

96.034.4053.9	129

96.034.4055.7	128

96.034.4151.4	152

96.034.4153.0	150

96.034.4153.1	151

96.034.4153.9	153

96.034.4155.7	152

96.034.5051.4	224

96.034.5053.0	222

96.034.5053.1	223

96.034.5053.9	225

96.034.5055.7	224

96.034.6051.4	202

96.034.6053.0	200

96.034.6053.1	201

96.034.6053.9	203

96.034.6055.7	202

96.035.2151.4	165

96.035.2153.0	162

96.035.2153.1	163

96.035.2153.9	166

96.035.2155.7	164

96.035.6151.4	169

96.035.6153.0	167

96.035.6153.1	168

96.035.6153.9	170

96.035.6155.7	169

96.036.2151.4	176

96.036.2153.0	173

96.036.2153.1	174

96.036.2153.9	177

96.036.2155.7	175

96.036.6151.4	180

96.036.6153.0	178

96.036.6153.1	179

96.036.6153.9	181

96.036.6155.7	180

96.041.4051.4	250

96.041.4053.0	248

96.041.4053.1	249

96.041.4153.0	259

96.041.4153.1	260

96.041.4253.0	249

96.041.4253.1	250

96.041.4353.0	260

96.041.4353.1	261

96.041.4553.0	268

96.041.4553.1	268

96.041.4851.4	274

96.041.4951.4	272

96.041.5051.4	297

96.041.5053.0	296

96.041.5053.1	297

96.041.6051.4	287

96.041.6053.0	286

96.041.6053.1	287

96.041.6151.4	277

96.041.6153.0	276

96.041.6153.1	277

96.042.4051.4	255

96.042.4053.0	254

96.042.4053.1	255

96.042.4153.0	264

96.042.4153.1	265

96.042.4553.0	270

96.042.4553.1	270

96.042.4851.4	275

96.042.4951.4	273

96.042.5051.4	302

96.042.5053.0	301

96.042.5053.1	302

96.042.6051.4	292

96.042.6053.0	291

96.042.6053.1	292

96.042.6151.4	282

96.042.6153.0	281

96.042.6153.1	282

96.043.4051.4	251

96.043.4053.0	248

96.043.4053.1	249

96.043.4153.0	259

96.043.4153.1	260

96.043.4851.4	274

96.043.4951.4	272

96.043.5051.4	298

96.043.5053.0	296

96.043.5053.1	297

96.043.6051.4	288

96.043.6053.0	286

96.043.6053.1	287

96.044.4051.4	256

96.044.4053.0	254

96.044.4053.1	255

96.044.4153.0	264

96.044.4153.1	265

96.044.4851.4	275

96.044.4951.4	273

96.044.5051.4	303

96.044.5053.0	301

96.044.5053.1	302

96.044.6051.4	293

96.044.6053.0	291

96.044.6053.1	292

96.045.6151.4	278

96.045.6153.0	276

96.045.6153.1	277

96.046.6151.4	283

96.046.6153.0	281

96.046.6153.1	282

96.050.0153.1	412

96.050.2153.1	412

96.051.4051.4	323

96.051.4053.0	320

96.051.4053.1	321

96.051.4053.6	322

96.051.4053.9	325

96.051.4151.4	341

96.051.4153.0	338

96.051.4153.1	339

96.051.4153.6	340

96.051.4153.9	342

96.051.4251.4	324

96.051.4253.0	321

96.051.4253.1	322

96.051.4253.6	323

96.051.4351.4	342

96.051.4353.0	339

96.051.4353.1	340

96.051.4353.6	341

96.051.4551.4	357

96.051.4553.0	356

96.051.4553.1	356

96.051.4553.6	357

96.051.4553.9	357

96.051.5051.4	398

96.051.5053.0	396

96.051.5053.1	397

96.051.5053.6	397

96.051.5053.9	399

96.051.6051.4	382

96.051.6053.0	380

96.051.6053.1	381

96.051.6053.6	381

96.051.6053.9	383

96.051.6151.4	366

96.051.6153.0	364

96.051.6153.1	365

96.051.6153.6	365

96.051.6153.9	367

96.052.4051.4	332

96.052.4053.0	330

96.052.4053.1	331

96.052.4053.6	331

96.052.4053.9	333

96.052.4151.4	350

96.052.4153.0	348

96.052.4153.1	349

96.052.4153.6	349

96.052.4153.9	351

96.052.4551.4	361

96.052.4553.0	360

96.052.4553.1	360

96.052.4553.6	361

96.052.4553.9	361

96.052.5051.4	406

96.052.5053.0	404

96.052.5053.1	405

96.052.5053.6	405

96.052.5053.9	407

96.052.6051.4	390

96.052.6053.0	388

96.052.6053.1	389

96.052.6053.6	389

96.052.6053.9	391

96.052.6151.4	374

96.052.6153.0	372

96.052.6153.1	373

96.052.6153.6	373

96.052.6153.9	375

96.053.4051.4	324

96.053.4053.0	320

96.053.4053.1	321

96.053.4053.6	323

96.053.4053.9	325

96.053.4151.4	342

96.053.4153.0	338

96.053.4153.1	339

96.053.4153.6	341

96.053.4153.9	343

96.053.6051.4	383

96.053.6053.0	380

96.053.6053.1	381

96.053.6053.6	382

96.053.6053.9	383

96.053.6251.4	399

96.053.6253.0	396

96.053.6253.1	397

96.053.6253.6	398

96.053.6253.9	399

96.054.4051.4	332

96.054.4053.0	330

96.054.4053.1	331

96.054.4053.6	332

96.054.4053.9	333

96.054.4151.4	350

96.054.4153.0	348

96.054.4153.1	349

96.054.4153.6	350

96.054.4153.9	351

96.054.6051.4	390

96.054.6053.0	388

96.054.6053.1	389

96.054.6053.6	390

96.054.6053.9	391

96.054.6251.4	406

96.054.6253.0	404

96.054.6253.1	405

96.054.6253.6	406

96.054.6253.9	407

96.055.6151.4	367

96.055.6153.0	364

96.055.6153.1	365

96.055.6153.6	366

96.055.6153.9	367

96.056.6151.4	374

96.056.6153.0	372

96.056.6153.1	373

96.056.6153.6	374

96.056.6153.9	375

96.131.0053.0	119

96.131.0053.1	120

96.131.0153.0	143

96.131.0153.1	144

96.131.1053.0	215

96.131.1053.1	216

96.131.2053.0	193

96.131.2053.1	194

96.131.2153.0	171

96.131.2153.1	172

96.131.4553.0	158

96.131.4553.1	158

96.132.0053.0	130

96.132.0053.1	131

96.132.0153.0	154

96.132.0153.1	155

96.132.1053.0	226

96.132.1053.1	227

96.132.2053.0	204

96.132.2053.1	205

96.132.2153.0	182

96.132.2153.1	183

96.132.4553.0	161

96.132.4553.1	161

96.133.0053.0	119

96.133.0053.1	120

96.133.0153.0	143

96.133.0153.1	144

96.133.1053.0	215

96.133.1053.1	216

96.133.2053.0	193

96.133.2053.1	194

96.134.0053.0	130

96.134.0053.1	131

96.134.0153.0	154

96.134.0153.1	155

96.134.1053.0	226

96.134.1053.1	227

96.134.2053.0	204

96.134.2053.1	205

96.135.2153.0	171

96.135.2153.1	172

96.136.2153.0	182

96.136.2153.1	183

96.141.0053.0	252

96.141.0053.1	253

96.141.0153.0	262

96.141.0153.1	263

96.141.1053.0	299

96.141.1053.1	300

96.141.2053.0	289

96.141.2053.1	290

96.141.2153.0	279

96.141.2153.1	280

96.141.4553.0	269

96.141.4553.1	269

96.142.0053.0	257

96.142.0053.1	258

96.142.0153.0	266

96.142.0153.1	267

96.142.1053.0	304

96.142.1053.1	305

96.142.2053.0	294

96.142.2053.1	295

96.142.2153.0	284

96.142.2153.1	285

96.142.4553.0	271

96.142.4553.1	271

96.143.0053.0	252

96.143.0053.1	253

96.143.0153.0	262

96.143.0153.1	263

96.143.2053.0	289

96.143.2053.1	290

96.143.2253.0	299

96.143.2253.1	300

96.144.0053.0	257

96.144.0053.1	258

96.144.0153.0	266

96.144.0153.1	267

96.144.2053.0	294

96.144.2053.1	295

96.144.2253.0	304

96.144.2253.1	305

96.145.2153.0	279

96.145.2153.1	280

96.146.2153.0	284

96.146.2153.1	285

96.151.0051.4	328

96.151.0053.0	326

96.151.0053.1	327

96.151.0053.6	327

96.151.0053.9	329

96.151.0151.4	346

96.151.0153.0	344

96.151.0153.1	345

96.151.0153.6	345

96.151.0153.9	347

96.151.0551.4	359

96.151.0553.0	358

96.151.0553.1	358

96.151.0553.6	359

96.151.0553.9	359

96.151.1051.4	402

96.151.1053.0	400

96.151.1053.1	401

96.151.1053.6	401

96.151.1053.9	403

96.151.2051.4	386

96.151.2053.0	384

96.151.2053.1	385

96.151.2053.6	385

96.151.2053.9	387

96.151.2151.4	370

96.151.2153.0	368

96.151.2153.1	369

96.151.2153.6	369

96.151.2153.9	371

96.152.0051.4	336

96.152.0053.0	334

96.152.0053.1	335

96.152.0053.6	335

96.152.0053.9	337

96.152.0151.4	354

96.152.0153.0	352

96.152.0153.1	353

96.152.0153.6	353

96.152.0153.9	355

96.152.0551.4	363

96.152.0553.0	362

96.152.0553.1	362

96.152.0553.6	363

96.152.0553.9	363

96.152.1051.4	410

96.152.1053.0	408

96.152.1053.1	409

96.152.1053.6	409

96.152.1053.9	411

96.152.2051.4	394

96.152.2053.0	392

96.152.2053.1	393

96.152.2053.6	393

96.152.2053.9	395

96.152.2151.4	378

96.152.2153.0	376

96.152.2153.1	377

96.152.2153.6	377

96.152.2153.9	379

96.153.0051.4	328

96.153.0053.0	326

96.153.0053.1	327

96.153.0053.6	328

96.153.0053.9	329

96.153.0151.4	346

96.153.0153.0	344

96.153.0153.1	345

96.153.0153.6	346

96.153.0153.9	347

96.153.2051.4	386

96.153.2053.0	384

96.153.2053.1	385

96.153.2053.6	386

96.153.2053.9	387

96.153.2251.4	402

96.153.2253.0	400

96.153.2253.1	401

96.153.2253.6	402

96.153.2253.9	403

96.154.0051.4	336

96.154.0053.0	334

96.154.0053.1	335

96.154.0053.6	336

96.154.0053.9	337

96.154.0151.4	354

96.154.0153.0	352

96.154.0153.1	353

96.154.0153.6	354

96.154.0153.9	355

96.154.2051.4	394

96.154.2053.0	392

96.154.2053.1	393

96.154.2053.6	394

96.154.2053.9	395

96.154.2251.4	410

96.154.2253.0	408

96.154.2253.1	409

96.154.2253.6	410

96.154.2253.9	411

96.155.2151.4	370

96.155.2153.0	368

96.155.2153.1	369

96.155.2153.6	370

96.155.2153.9	371

96.156.2151.4	378

96.156.2153.0	376

96.156.2153.1	377

96.156.2153.6	378

96.156.2153.9	379

96.222.x000.1	98

96.222.x002.4	98

96.222.x003.1	98

96.222.x004.1	99

96.222.x007.4	99

96.222.x008.4	99

96.222.x030.1	101

96.222.x032.4	101

96.222.x033.1	101

96.222.x034.1	102

96.222.x037.4	102

96.222.x038.4	102

96.222.x092.4	104

96.222.x092.8	104

96.222.x097.4	104

96.222.x097.8	105

96.222.x098.4	105

96.222.x098.8	105

96.223.x092.4	106

96.223.x092.8	106

96.223.x097.4	106

96.223.x097.8	107

96.223.x098.4	107

96.223.x098.8	107

96.232.x000.1	237

96.232.x001.7	237

96.232.x003.1	237

96.232.x004.1	238

96.232.x005.7	238

96.232.x006.7	238

96.232.x030.1	240

96.232.x031.7	240

96.232.x033.1	240

96.232.x034.1	241

96.232.x035.7	241

96.232.x036.7	241

96.233.x000.1	244

96.233.x001.7	244

96.233.x003.1	244

96.233.x004.1	245

96.233.x005.7	245

96.233.x006.7	245

96.233.x030.1	246

96.233.x031.7	246

96.233.x033.1	246

96.233.x034.1	247

96.233.x035.7	247

96.233.x036.7	247

96.442.x000.1	313

96.442.x003.1	313

96.442.x004.1	314

96.442.x030.1	315

96.442.x033.1	315

96.442.x034.1	315

96.442.x080.1	318

96.442.x083.1	318

96.442.x084.1	318

96.443.x000.1	316

96.443.x003.1	316

96.443.x004.1	316

96.443.x030.1	317

96.443.x033.1	317

96.443.x034.1	317

96.443.x082.4	319

96.443.x087.4	319

96.443.x088.4	319

96.452.x000.1	418

96.452.x000.6	418

96.452.x003.1	418

96.452.x003.6	419

96.452.x004.1	419

96.452.x004.6	419

96.452.x030.1	420

96.452.x030.6	420

96.452.x033.1	420

96.452.x033.6	421

96.452.x034.1	421

96.452.x034.6	421

96.453.x000.1	422

96.453.x000.6	422

96.453.x003.1	422

96.453.x003.6	423

96.453.x004.1	423

96.453.x004.6	423

96.453.x030.1	424

96.453.x030.6	424

96.453.x033.1	424

96.453.x033.6	425

96.453.x034.1	425

96.453.x034.6	425

96.453.x080.1	430

96.453.x083.1	430

96.453.x084.1	430

96.454.x000.1	426

96.454.x000.6	426

96.454.x003.1	426

96.454.x003.6	427

96.454.x004.1	427

96.454.x004.6	427

96.454.x030.1	428

96.454.x030.6	428

96.454.x033.1	428

96.454.x033.6	429

96.454.x034.1	429

96.454.x034.6	429

99.413.6205.2	96, 233

99.414.6205.2	96, 233

99.415.6205.2	95, 232

99.416.6205.2	95, 232

99.529.0000.7	309, 414

99.530.0000.7	309, 414

99.531.0000.7	308, 413

99.532.0000.7	308, 413

99.537.0000.7	92

99.708.0000.7	103

99.709.0000.7	103

99.710.0000.7	100

99.711.0000.7	100

99.712.0000.7	242

99.713.0000.7	242

99.714.0000.7	239

99.715.0000.7	239

99.716.0000.7	242

99.717.0000.7	243

99.718.0000.7	243

99.906.0000.7	231

99.910.0000.7	92

99.911.0000.7	306

99.916.0000.7	307

99.929.0000.7	231

99.935.0000.7	306

99.936.0000.7	307

99.946.0000.7	94

Z5.564.4553.0	96, 233

Z5.564.4553.1	96, 233

Z5.565.9853.0	309, 414

Z5.565.9953.1	309, 414